## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Which of the following carrier frequencies is illegal for LSB AFSK emissions on the 17 meter band RTTY and data segment of 18.068 to 18.110 MHz?
A. 18.068 MHz
B. 18.100 MHz
C. 18.107 MHz
D. 18.110 MHz
FCC Rule: [97.305, 97.307(b)] E1A01 ECLM Page (3 - 4)

## Slide 4: Which of the following carrier frequencies is illegal for LSB AFSK emissions on the 17 meter band RTTY and data segment of 18.068 to 18.110 MHz?
A. 18.068 MHz
B. 18.100 MHz
C. 18.107 MHz
D. 18.110 MHz
(A) FCC Rule: [97.305, 97.307(b)] E1A01 ECLM Page (3 - 4)

## Slide 5: When using a transceiver that displays the carrier frequency of phone signals, which of the following displayed frequencies represents the lowest frequency at which a properly adjusted LSB emission will be totally within the band?
A. The exact lower band edge
B. 300 Hz above the lower band edge
C. 1 kHz above the lower band edge
D. 3 kHz above the lower band edge
FCC Rule: [97.301, 97.305] E1A02 ECLM Page (3 - 4)

## Slide 6: When using a transceiver that displays the carrier frequency of phone signals, which of the following displayed frequencies represents the lowest frequency at which a properly adjusted LSB emission will be totally within the band?
A. The exact lower band edge
B. 300 Hz above the lower band edge
C. 1 kHz above the lower band edge
D. 3 kHz above the lower band edge
(D) FCC Rule: [97.301, 97.305] E1A02 ECLM Page (3 - 4)

## Slide 7: What is the maximum legal carrier frequency on the 20 meter band for transmitting USB AFSK digital signals having a 1 kHz bandwidth?
A. 14.070 MHz
B. 14.100 MHz
C. 14.149 MHz
D. 14.349 MHz
FCC Rule: [97.305, 97.307(b)] E1A03 ECLM Page (3 - 4)

## Slide 8: What is the maximum legal carrier frequency on the 20 meter band for transmitting USB AFSK digital signals having a 1 kHz bandwidth?
A. 14.070 MHz
B. 14.100 MHz
C. 14.149 MHz
D. 14.349 MHz
(C) FCC Rule: [97.305, 97.307(b)] E1A03 ECLM Page (3 - 4)

## Slide 9: With your transceiver displaying the carrier frequency of phone signals, you hear a DX station calling CQ on 3.601 MHz LSB. Is it legal to return the call using lower sideband on the same frequency?
A. Yes, because the DX station initiated the contact
B. Yes, because the displayed frequency is within the 75 meter phone band segment
C. No, the sideband will extend beyond the edge of the phone band segment
D. No, U.S. stations are not permitted to use phone emissions below 3.610 MHz
FCC Rule: [97.301, 97.305] E1A04 ECLM Page (3 - 4)

## Slide 10: With your transceiver displaying the carrier frequency of phone signals, you hear a DX station calling CQ on 3.601 MHz LSB. Is it legal to return the call using lower sideband on the same frequency?
A. Yes, because the DX station initiated the contact
B. Yes, because the displayed frequency is within the 75 meter phone band segment
C. No, the sideband will extend beyond the edge of the phone band segment
D. No, U.S. stations are not permitted to use phone emissions below 3.610 MHz
(C) FCC Rule: [97.301, 97.305] E1A04 ECLM Page (3 - 4)

## Slide 11: What is the maximum power output permitted on the 60 meter band?
A. 50 watts PEP effective radiated power relative to an isotropic radiator
B. 50 watts PEP effective radiated power relative to a dipole
C. 100 watts PEP effective radiated power relative to the gain of a half-wave dipole
D. 100 watts PEP effective radiated power relative to an isotropic radiator
FCC Rule: [97.313] E1A05 ECLM Page (3 - 4)

## Slide 12: What is the maximum power output permitted on the 60 meter band?
A. 50 watts PEP effective radiated power relative to an isotropic radiator
B. 50 watts PEP effective radiated power relative to a dipole
C. 100 watts PEP effective radiated power relative to the gain of a half-wave dipole
D. 100 watts PEP effective radiated power relative to an isotropic radiator
(C) FCC Rule: [97.313] E1A05 ECLM Page (3 - 4)

## Slide 13: Where must the carrier frequency of a CW signal be set to comply with FCC rules for 60 meter operation?
A. At the lowest frequency of the channel
B. At the center frequency of the channel
C. At the highest frequency of the channel
D. On any frequency where the signal’s sidebands are within the channel
FCC Rule: [97.303(h)(1)] E1A06 ECLM Page (3 - 4)

## Slide 14: Where must the carrier frequency of a CW signal be set to comply with FCC rules for 60 meter operation?
A. At the lowest frequency of the channel
B. At the center frequency of the channel
C. At the highest frequency of the channel
D. On any frequency where the signal’s sidebands are within the channel
(B) FCC Rule: [97.303(h)(1)] E1A06 ECLM Page (3 - 4)

## Slide 15: What is the maximum power permitted on the 2200 meter band?
A. 50 watts PEP
B. 100 watts PEP
C. 1 watt EIRP (Equivalent isotropic radiated power)
D. 5 watts EIRP (Equivalent isotropic radiated power)
FCC Rule: [97.313(k)] E1A07 ECLM Page (3 - 5)

## Slide 16: What is the maximum power permitted on the 2200 meter band?
A. 50 watts PEP
B. 100 watts PEP
C. 1 watt EIRP (Equivalent isotropic radiated power)
D. 5 watts EIRP (Equivalent isotropic radiated power)
(C) FCC Rule: [97.313(k)] E1A07 ECLM Page (3 - 5)

## Slide 17: If a station in a message forwarding system inadvertently forwards a message that is in violation of FCC rules, who is primarily accountable for the rules violation?
A. The control operator of the packet bulletin board station
B. The control operator of the originating station
C. The control operators of all the stations in the system
D. The control operators of all the stations in the system not authenticating the source from which they accept communications
FCC Rule: [97.219] E1A08 ECLM Page (3 - 5)

## Slide 18: If a station in a message forwarding system inadvertently forwards a message that is in violation of FCC rules, who is primarily accountable for the rules violation?
A. The control operator of the packet bulletin board station
B. The control operator of the originating station
C. The control operators of all the stations in the system
D. The control operators of all the stations in the system not authenticating the source from which they accept communications
(B) FCC Rule: [97.219] E1A08 ECLM Page (3 - 5)

## Slide 19: What action or actions should you take if your digital message forwarding station inadvertently forwards a communication that violates FCC rules?
A. Discontinue forwarding the communication as soon as you become aware of it
B. Notify the originating station that the communication does not comply with FCC rules
C. Notify the nearest FCC Field Engineer’s office
D. All these choices are correct
FCC Rule: [97.219] E1A09 ECLM Page (3 - 6)

## Slide 20: What action or actions should you take if your digital message forwarding station inadvertently forwards a communication that violates FCC rules?
A. Discontinue forwarding the communication as soon as you become aware of it
B. Notify the originating station that the communication does not comply with FCC rules
C. Notify the nearest FCC Field Engineer’s office
D. All these choices are correct
(A) FCC Rule: [97.219] E1A09 ECLM Page (3 - 6)

## Slide 21: If an amateur station is installed aboard a ship or aircraft, what condition must be met before the station is operated?
A. Its operation must be approved by the master of the ship or the pilot in command of the aircraft
B. The amateur station operator must agree not to transmit when the main radio of the ship or aircraft is in use
C. The amateur station must have a power supply that is completely independent of the main ship or aircraft power supply
D. The amateur operator must have an FCC Marine or Aircraft endorsement on his or her amateur license
FCC Rule: [97.11] E1A10 ECLM Page (3 - 6)

## Slide 22: If an amateur station is installed aboard a ship or aircraft, what condition must be met before the station is operated?
A. Its operation must be approved by the master of the ship or the pilot in command of the aircraft
B. The amateur station operator must agree not to transmit when the main radio of the ship or aircraft is in use
C. The amateur station must have a power supply that is completely independent of the main ship or aircraft power supply
D. The amateur operator must have an FCC Marine or Aircraft endorsement on his or her amateur license
(A) FCC Rule: [97.11] E1A10 ECLM Page (3 - 6)

## Slide 23: Which of the following describes authorization or licensing required when operating an amateur station aboard a U.S.-registered vessel in international waters?
A. Any amateur license with an FCC Marine or Aircraft endorsement
B. Any FCC-issued amateur license
C. Only General Class or higher amateur licenses
D. An unrestricted Radiotelephone Operator Permit
FCC Rule: [97.5] E1A11 ECLM Page (3 - 6)

## Slide 24: Which of the following describes authorization or licensing required when operating an amateur station aboard a U.S.-registered vessel in international waters?
A. Any amateur license with an FCC Marine or Aircraft endorsement
B. Any FCC-issued amateur license
C. Only General Class or higher amateur licenses
D. An unrestricted Radiotelephone Operator Permit
(B) FCC Rule: [97.5] E1A11 ECLM Page (3 - 6)

## Slide 25: What special operating frequency restrictions are imposed on slow scan TV transmissions?
A. None; they are allowed on all amateur frequencies
B. They are restricted to 7.245 MHz, 14.245 MHz, 21.345 MHz, and 28.945 MHz
C. They are restricted to phone band segments
D. They are not permitted above 54 MHz
E1A12 ECLM Page (8 - 21)

## Slide 26: What special operating frequency restrictions are imposed on slow scan TV transmissions?
A. None; they are allowed on all amateur frequencies
B. They are restricted to 7.245 MHz, 14.245 MHz, 21.345 MHz, and 28.945 MHz
C. They are restricted to phone band segments
D. They are not permitted above 54 MHz
(C) E1A12 ECLM Page (8 - 21)

## Slide 27: Who must be in physical control of the station apparatus of an amateur station aboard any vessel or craft that is documented or registered in the United States?
A. Only a person with an FCC Marine Radio license grant
B. Any person holding an FCC issued amateur license or who is authorized for alien reciprocal operation
C. Only a person named in an amateur station license grant
D. Any person named in an amateur station license grant or a person holding an unrestricted Radiotelephone Operator Permit
FCC Rule: [97.5] E1A13 ECLM Page (3 - 6)

## Slide 28: Who must be in physical control of the station apparatus of an amateur station aboard any vessel or craft that is documented or registered in the United States?
A. Only a person with an FCC Marine Radio license grant
B. Any person holding an FCC issued amateur license or who is authorized for alien reciprocal operation
C. Only a person named in an amateur station license grant
D. Any person named in an amateur station license grant or a person holding an unrestricted Radiotelephone Operator Permit
(B) FCC Rule: [97.5] E1A13 ECLM Page (3 - 6)

## Slide 29: Except in some parts of Alaska, what is the maximum power permitted on the 630 meter band?
A. 50 watts PEP
B. 100 watts PEP
C. 1 watt EIRP
D. 5 watts EIRP
FCC Rule: [97.313(1)] E1A14 ECLM Page (3 - 6)

## Slide 30: Except in some parts of Alaska, what is the maximum power permitted on the 630 meter band?
A. 50 watts PEP
B. 100 watts PEP
C. 1 watt EIRP
D. 5 watts EIRP
(D) FCC Rule: [97.313(1)] E1A14 ECLM Page (3 - 6)

## Slide 31: Which of the following constitutes a spurious emission?
A. An amateur station transmission made without the proper call sign identification
B. A signal transmitted to prevent its detection by any station other than the intended recipient
C. Any transmitted signal that unintentionally interferes with another licensed radio station
D. An emission outside the signal's necessary bandwidth that can be reduced or eliminated without affecting the information transmitted
FCC Rule: [97.3] E1B01 ECLM Page (3 - 7)

## Slide 32: Which of the following constitutes a spurious emission?
A. An amateur station transmission made without the proper call sign identification
B. A signal transmitted to prevent its detection by any station other than the intended recipient
C. Any transmitted signal that unintentionally interferes with another licensed radio station
D. An emission outside the signal's necessary bandwidth that can be reduced or eliminated without affecting the information transmitted
(D) FCC Rule: [97.3] E1B01 ECLM Page (3 - 7)

## Slide 33: Which of the following is an acceptable bandwidth for Digital Radio Mondiale (DRM) based voice or SSTV digital transmissions made on the HF amateur bands?
A. 3 kHz
B. 10 kHz
C. 15 kHz
D. 20 kHz
FCC Rule: [97.302(f)(2)] E1B02 ECLM Page (8 - 23)

## Slide 34: Which of the following is an acceptable bandwidth for Digital Radio Mondiale (DRM) based voice or SSTV digital transmissions made on the HF amateur bands?
A. 3 kHz
B. 10 kHz
C. 15 kHz
D. 20 kHz
(A) FCC Rule: [97.302(f)(2)] E1B02 ECLM Page (8 - 23)

## Slide 35: Within what distance must an amateur station protect an FCC monitoring facility from harmful interference?
A. 1 mile
B. 3 miles
C. 10 miles
D. 30 miles
FCC Rule: [97.13] E1B03 ECLM Page (3 - 8)

## Slide 36: Within what distance must an amateur station protect an FCC monitoring facility from harmful interference?
A. 1 mile
B. 3 miles
C. 10 miles
D. 30 miles
(A) FCC Rule: [97.13] E1B03 ECLM Page (3 - 8)

## Slide 37: What must be done before placing an amateur station within an officially designated wilderness area or wildlife preserve, or an area listed in the National Register of Historic Places?
A. A proposal must be submitted to the National Park Service
B. A letter of intent must be filed with the Environmental Protection Agency
C. An Environmental Assessment must be submitted to the FCC
D. A form FSD-15 must be submitted to the Department of the Interior
FCC Rule: [97.13, 1.1305-1.1319] E1B04 ECLM Page (3 - 8)

## Slide 38: What must be done before placing an amateur station within an officially designated wilderness area or wildlife preserve, or an area listed in the National Register of Historic Places?
A. A proposal must be submitted to the National Park Service
B. A letter of intent must be filed with the Environmental Protection Agency
C. An Environmental Assessment must be submitted to the FCC
D. A form FSD-15 must be submitted to the Department of the Interior
(C) FCC Rule: [97.13, 1.1305-1.1319] E1B04 ECLM Page (3 - 8)

## Slide 39: What is the National Radio Quiet Zone?
A. An area in Puerto Rico surrounding the Arecibo Radio Telescope
B. An area in New Mexico surrounding the White Sands Test Area
C. An area surrounding the National Radio Astronomy Observatory
D. An area in Florida surrounding Cape Canaveral
FCC Rule: [97.3] E1B05 ECLM Page (3 - 20)

## Slide 40: What is the National Radio Quiet Zone?
A. An area in Puerto Rico surrounding the Arecibo Radio Telescope
B. An area in New Mexico surrounding the White Sands Test Area
C. An area surrounding the National Radio Astronomy Observatory
D. An area in Florida surrounding Cape Canaveral
(C) FCC Rule: [97.3] E1B05 ECLM Page (3 - 20)

## Slide 41: Which of the following additional rules apply if you are installing an amateur station antenna at a site at or near a public use airport?
A. You may have to notify the Federal Aviation Administration and register it with the FCC as required by Part 17 of the FCC rules
B. You must submit engineering drawings to the FAA
C. You must file an Environmental Impact Statement with the EPA before construction begins
D. You must obtain a construction permit from the airport zoning authority
FCC Rule: [97.15] E1B06 ECLM Page (3 - 9)

## Slide 42: Which of the following additional rules apply if you are installing an amateur station antenna at a site at or near a public use airport?
A. You may have to notify the Federal Aviation Administration and register it with the FCC as required by Part 17 of the FCC rules
B. You must submit engineering drawings to the FAA
C. You must file an Environmental Impact Statement with the EPA before construction begins
D. You must obtain a construction permit from the airport zoning authority
(A) FCC Rule: [97.15] E1B06 ECLM Page (3 - 9)

## Slide 43: To what type of regulations does PRB-1 apply?
A. Homeowners associations
B. FAA tower height limits
C. State and local zoning
D. Use of wireless devices in vehicles
FCC Rule: [97.15] E1B07 ECLM Page (3 - 8)

## Slide 44: To what type of regulations does PRB-1 apply?
A. Homeowners associations
B. FAA tower height limits
C. State and local zoning
D. Use of wireless devices in vehicles
(C) FCC Rule: [97.15] E1B07 ECLM Page (3 - 8)

## Slide 45: What limitations may the FCC place on an amateur station if its signal causes interference to domestic broadcast reception, assuming that the receivers involved are of good engineering design?
A. The amateur station must cease operation
B. The amateur station must cease operation on all frequencies below 30 MHz
C. The amateur station must cease operation on all frequencies above 30 MHz
D. The amateur station must avoid transmitting during certain hours on frequencies that cause the interference
FCC Rule: [97.121] E1B08 ECLM Page (3 - 7)

## Slide 46: What limitations may the FCC place on an amateur station if its signal causes interference to domestic broadcast reception, assuming that the receivers involved are of good engineering design?
A. The amateur station must cease operation
B. The amateur station must cease operation on all frequencies below 30 MHz
C. The amateur station must cease operation on all frequencies above 30 MHz
D. The amateur station must avoid transmitting during certain hours on frequencies that cause the interference
(D) FCC Rule: [97.121] E1B08 ECLM Page (3 - 7)

## Slide 47: Which amateur stations may be operated under RACES rules?
A. Only those club stations licensed to Amateur Extra Class operators
B. Any FCC-licensed amateur station except a Technician Class
C. Any FCC-licensed amateur station certified by the responsible civil defense organization for the area served
D. Any FCC-licensed amateur station participating in the Military Auxiliary Radio System (MARS)
FCC Rule: [97.407] E1B09 ECLM Page (3 - 6)

## Slide 48: Which amateur stations may be operated under RACES rules?
A. Only those club stations licensed to Amateur Extra Class operators
B. Any FCC-licensed amateur station except a Technician Class
C. Any FCC-licensed amateur station certified by the responsible civil defense organization for the area served
D. Any FCC-licensed amateur station participating in the Military Auxiliary Radio System (MARS)
(C) FCC Rule: [97.407] E1B09 ECLM Page (3 - 6)

## Slide 49: What frequencies are authorized to an amateur station operating under RACES rules?
A. All amateur service frequencies authorized to the control operator
B. Specific segments in the amateur service MF, HF, VHF and UHF bands
C. Specific local government channels
D. Military Auxiliary Radio System (MARS) channels
FCC Rule: [97.407] E1B10 ECLM Page (3 - 6)

## Slide 50: What frequencies are authorized to an amateur station operating under RACES rules?
A. All amateur service frequencies authorized to the control operator
B. Specific segments in the amateur service MF, HF, VHF and UHF bands
C. Specific local government channels
D. Military Auxiliary Radio System (MARS) channels
(A) FCC Rule: [97.407] E1B10 ECLM Page (3 - 6)

## Slide 51: What does PRB-1 require of regulations affecting amateur radio?
A. No limitations may be placed on antenna size or placement
B. Reasonable accommodations of amateur radio must be made
C. Amateur radio operations must be permitted in any private residence
D. Use of wireless devices in a vehicle is exempt from regulation
FCC Rule: [97.15] E1B11 ECLM Page (3 - 8)

## Slide 52: What does PRB-1 require of regulations affecting amateur radio?
A. No limitations may be placed on antenna size or placement
B. Reasonable accommodations of amateur radio must be made
C. Amateur radio operations must be permitted in any private residence
D. Use of wireless devices in a vehicle is exempt from regulation
(B) FCC Rule: [97.15] E1B11 ECLM Page (3 - 8)

## Slide 53: What must the control operator of a repeater operating in the 70 cm band do if a radiolocation system experiences interference from that repeater?
A. Cease operation or make changes to the repeater to mitigate the interference
B. File an FAA NOTAM (Notice to Airmen) with the repeater system's ERP, call sign, and six-character grid locator
C. Reduce the repeater antenna HAAT (Height Above Average Terrain)
D. All these choices are correct
FCC Rule: [97.303(b)] E1B12 ECLM Page (3 - 19)

## Slide 54: What must the control operator of a repeater operating in the 70 cm band do if a radiolocation system experiences interference from that repeater?
A. Cease operation or make changes to the repeater to mitigate the interference
B. File an FAA NOTAM (Notice to Airmen) with the repeater system's ERP, call sign, and six-character grid locator
C. Reduce the repeater antenna HAAT (Height Above Average Terrain)
D. All these choices are correct
(A) FCC Rule: [97.303(b)] E1B12 ECLM Page (3 - 19)

## Slide 55: What is the maximum bandwidth for a data emission on 60 meters?
A. 60 Hz
B. 170 Hz
C. 1.5 kHz
D. 2.8 kHz
FCC Rule: [97.303] E1C01 ECLM Page (3 - 4)

## Slide 56: What is the maximum bandwidth for a data emission on 60 meters?
A. 60 Hz
B. 170 Hz
C. 1.5 kHz
D. 2.8 kHz
(D) FCC Rule: [97.303] E1C01 ECLM Page (3 - 4)

## Slide 57: Which of the following types of communications may be transmitted to amateur stations in foreign countries?
A. Business-related messages for non-profit organizations
B. Messages intended for users of the maritime satellite service
C. Communications incidental to the purpose of the amateur service and remarks of a personal nature
D. All of these choices are correct
FCC Rule: [97.117] E1C02 ECLM Page (3 - 20)

## Slide 58: Which of the following types of communications may be transmitted to amateur stations in foreign countries?
A. Business-related messages for non-profit organizations
B. Messages intended for users of the maritime satellite service
C. Communications incidental to the purpose of the amateur service and remarks of a personal nature
D. All of these choices are correct
(C) FCC Rule: [97.117] E1C02 ECLM Page (3 - 20)

## Slide 59: How do the control operator responsibilities of a station under automatic control differ from one under local control?
A. Under local control there is no control operator
B. Under automatic control the control operator is not required to be present at the control point
C. Under automatic control there is no control operator
D. Under local control a control operator is not required to be present at a control point
FCC Rule: [97.3, 97.109(d)] E1C03 ECLM Page (3 - 12)

## Slide 60: How do the control operator responsibilities of a station under automatic control differ from one under local control?
A. Under local control there is no control operator
B. Under automatic control the control operator is not required to be present at the control point
C. Under automatic control there is no control operator
D. Under local control a control operator is not required to be present at a control point
(B) FCC Rule: [97.3, 97.109(d)] E1C03 ECLM Page (3 - 12)

## Slide 61: What is meant by IARP?
A. An international amateur radio permit that allows U.S. amateurs to operate in certain countries of the Americas
B. The internal amateur radio practices policy of the FCC
C. An indication of increased antenna reflected power.
D. A forecast of intermittent aurora radio propagation
E1C04 ECLM Page (3 - 21)

## Slide 62: What is meant by IARP?
A. An international amateur radio permit that allows U.S. amateurs to operate in certain countries of the Americas
B. The internal amateur radio practices policy of the FCC
C. An indication of increased antenna reflected power.
D. A forecast of intermittent aurora radio propagation
(A) E1C04 ECLM Page (3 - 21)

## Slide 63: Removed from question pool When may an automatically controlled station originate third party communications?
A. Never
B. Only when transmitting RTTY or data emissions
C. When agreed upon by the sending or receiving station
D. When approved by the National Telecommunication and Information Administration
FCC Rule: [97.221(c)(1), 97.115(c)] E1C05 ECLM Page (3 - 12)

## Slide 64: Removed from question pool When may an automatically controlled station originate third party communications?
A. Never
B. Only when transmitting RTTY or data emissions
C. When agreed upon by the sending or receiving station
D. When approved by the National Telecommunication and Information Administration
(A) FCC Rule: [97.221(c)(1), 97.115(c)] E1C05 ECLM Page (3 - 12)

## Slide 65: Which of the following is required in order to operate in accordance with CEPT rules in foreign countries where permitted?
A. You must identify in the official language of the country in which you are operating
B. The U.S. embassy must approve of your operation
C. You must bring a copy of FCC Public Notice DA 16-1048
D. You must append "/CEPT" to your call sign
E1C06 ECLM Page (3 - 21)

## Slide 66: Which of the following is required in order to operate in accordance with CEPT rules in foreign countries where permitted?
A. You must identify in the official language of the country in which you are operating
B. The U.S. embassy must approve of your operation
C. You must bring a copy of FCC Public Notice DA 16-1048
D. You must append "/CEPT" to your call sign
(C) E1C06 ECLM Page (3 - 21)

## Slide 67: At what level below a signal's mean power level is its bandwidth determined according to FCC rules?
A. 3 dB
B. 6 dB
C. 23 dB
D. 26 dB
FCC Rule: [97.3(a)(8)] E1C07 ECLM Page (3 - 4)

## Slide 68: At what level below a signal's mean power level is its bandwidth determined according to FCC rules?
A. 3 dB
B. 6 dB
C. 23 dB
D. 26 dB
(D) FCC Rule: [97.3(a)(8)] E1C07 ECLM Page (3 - 4)

## Slide 69: What is the maximum permissible duration of a remotely controlled station’s transmissions if its control link malfunctions?
A. 30 seconds
B. 3 minutes
C. 5 minutes
D. 10 minutes
FCC Rule: [97.213] E1C08 ECLM Page (3 - 10)

## Slide 70: What is the maximum permissible duration of a remotely controlled station’s transmissions if its control link malfunctions?
A. 30 seconds
B. 3 minutes
C. 5 minutes
D. 10 minutes
(B) FCC Rule: [97.213] E1C08 ECLM Page (3 - 10)

## Slide 71: What is the highest modulation index permitted at the highest modulation frequency for angle modulation below 29.0 MHz?
A. 0.5
B. 1.0
C. 2.0
D. 3.0
FCC Rule: [97.307] E1C09 ECLM Page (8 - 4)

## Slide 72: What is the highest modulation index permitted at the highest modulation frequency for angle modulation below 29.0 MHz?
A. 0.5
B. 1.0
C. 2.0
D. 3.0
(B) FCC Rule: [97.307] E1C09 ECLM Page (8 - 4)

## Slide 73: What is the permitted mean power of any spurious emission relative to the mean power of the fundamental emission from a station transmitter or external RF amplifier installed after January 1, 2003 and transmitting on a frequency below 30 MHz?
A. At least 43 dB below
B. At least 53 dB below
C. At least 63 dB below
D. At least 73 dB below
FCC Rule: [97.307] E1C10 ECLM Page (3 - 7)

## Slide 74: What is the permitted mean power of any spurious emission relative to the mean power of the fundamental emission from a station transmitter or external RF amplifier installed after January 1, 2003 and transmitting on a frequency below 30 MHz?
A. At least 43 dB below
B. At least 53 dB below
C. At least 63 dB below
D. At least 73 dB below
(A) FCC Rule: [97.307] E1C10 ECLM Page (3 - 7)

## Slide 75: Which of the following operating arrangements allows an FCC-licensed U.S. citizen to operate in many European countries, and alien amateurs from many European countries to operate in the U.S.?
A. CEPT agreement
B. IARP agreement
C. ITU reciprocal license
D. All these choices are correct
FCC Rule: [97.5] E1C11 ECLM Page (3 - 21)

## Slide 76: Which of the following operating arrangements allows an FCC-licensed U.S. citizen to operate in many European countries, and alien amateurs from many European countries to operate in the U.S.?
A. CEPT agreement
B. IARP agreement
C. ITU reciprocal license
D. All these choices are correct
(A) FCC Rule: [97.5] E1C11 ECLM Page (3 - 21)

## Slide 77: On what portion of the 630 meter band are phone emissions permitted?
A. None
B. Only the top 3 kHz
C. Only the bottom 3 kHz
D. The entire band
FCC Rule: [97.305(c)] E1C12 ECLM Page (3 - 5)

## Slide 78: On what portion of the 630 meter band are phone emissions permitted?
A. None
B. Only the top 3 kHz
C. Only the bottom 3 kHz
D. The entire band
(D) FCC Rule: [97.305(c)] E1C12 ECLM Page (3 - 5)

## Slide 79: What notifications must be given before transmitting on the 630 meter or 2200 meter bands?
A. A special endorsement must be requested from the FCC
B. An environmental impact statement must be filed with the Department of the Interior
C. Operators must inform the Utilities Technology Council (UTC) of their call sign and coordinates of the station
D. Operators must inform the FAA of their intent to operate, giving their call sign and distance to the nearest runway
FCC Rule: [97.303(g)] E1C13 ECLM Page (3 - 5)

## Slide 80: What notifications must be given before transmitting on the 630 meter or 2200 meter bands?
A. A special endorsement must be requested from the FCC
B. An environmental impact statement must be filed with the Department of the Interior
C. Operators must inform the Utilities Technology Council (UTC) of their call sign and coordinates of the station
D. Operators must inform the FAA of their intent to operate, giving their call sign and distance to the nearest runway
(C) FCC Rule: [97.303(g)] E1C13 ECLM Page (3 - 5)

## Slide 81: How long must an operator wait after filing a notification with the Utilities Technology Council (UTC) before operating on the 2200 meter or 630 meter band?
A. Operators must not operate until approval is received
B. Operators may operate after 30 days, providing they have not been told that their station is within 1 km of PLC systems using those frequencies
C. Operators may not operate until a test signal has been transmitted in coordination with the local power company
D. Operations may commence immediately, and may continue unless interference is reported by the UTC
FCC Rule: [97.303(g)] E1C14 ECLM Page (3 - 5)

## Slide 82: How long must an operator wait after filing a notification with the Utilities Technology Council (UTC) before operating on the 2200 meter or 630 meter band?
A. Operators must not operate until approval is received
B. Operators may operate after 30 days, providing they have not been told that their station is within 1 km of PLC systems using those frequencies
C. Operators may not operate until a test signal has been transmitted in coordination with the local power company
D. Operations may commence immediately, and may continue unless interference is reported by the UTC
(B) FCC Rule: [97.303(g)] E1C14 ECLM Page (3 - 5)