## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Which of the following digital modes is designed for meteor scatter communications?
A. WSPR
B. MSK144
C. Hellschreiber
D. APRS
E2D01 ECLM Page (10 - 16)

## Slide 4: Which of the following digital modes is designed for meteor scatter communications?
A. WSPR
B. MSK144
C. Hellschreiber
D. APRS
(B) E2D01 ECLM Page (10 - 16)

## Slide 5: Which of the following is a good technique for making meteor scatter contacts?
A. 15-second timed transmission sequences with stations alternating based on location
B. Use of special digital modes
C. Short transmissions with rapidly repeated call signs and signal reports
D. All these choices are correct
E2D02 ECLM Page (10 - 16)

## Slide 6: Which of the following is a good technique for making meteor scatter contacts?
A. 15-second timed transmission sequences with stations alternating based on location
B. Use of special digital modes
C. Short transmissions with rapidly repeated call signs and signal reports
D. All these choices are correct
(D) E2D02 ECLM Page (10 - 16)

## Slide 7: Which of the following digital modes is especially useful for EME communications?
A. MSK144
B. PACTOR III
C. Olivia
D. JT65
E2D03 ECLM Page (10 - 17)

## Slide 8: Which of the following digital modes is especially useful for EME communications?
A. MSK144
B. PACTOR III
C. Olivia
D. JT65
(D) E2D03 ECLM Page (10 - 17)

## Slide 9: What technology is used to track, in real time, balloons carrying amateur radio transmitters?
A. Ultrasonics
B. Bandwidth compressed LORAN
C. APRS
D. Doppler shift of beacon signals
E2D04 ECLM Page (8 - 12)

## Slide 10: What technology is used to track, in real time, balloons carrying amateur radio transmitters?
A. Ultrasonics
B. Bandwidth compressed LORAN
C. APRS
D. Doppler shift of beacon signals
(C) E2D04 ECLM Page (8 - 12)

## Slide 11: What is one advantage of the JT65 mode?
A. Uses only a 65 Hz bandwidth
B. The ability to decode signals which have a very low signal to noise ratio
C. Easily copied by ear if necessary
D. Permits fast-scan TV transmissions over narrow bandwidth
E2D05 ECLM Page (10 - 17)

## Slide 12: What is one advantage of the JT65 mode?
A. Uses only a 65 Hz bandwidth
B. The ability to decode signals which have a very low signal to noise ratio
C. Easily copied by ear if necessary
D. Permits fast-scan TV transmissions over narrow bandwidth
(B) E2D05 ECLM Page (10 - 17)

## Slide 13: Which of the following describes a method of establishing EME contacts?
A. Time synchronous transmissions alternately from each station
B. Storing and forwarding digital messages
C. Judging optimum transmission times by monitoring beacons reflected from the moon
D. High speed CW identification to avoid fading
E2D06 ECLM Page (10 - 17)

## Slide 14: Which of the following describes a method of establishing EME contacts?
A. Time synchronous transmissions alternately from each station
B. Storing and forwarding digital messages
C. Judging optimum transmission times by monitoring beacons reflected from the moon
D. High speed CW identification to avoid fading
(A) E2D06 ECLM Page (10 - 17)

## Slide 15: What digital protocol is used by APRS?
A. PACTOR
B. 802.11
C. AX.25
D. AMTOR
E2D07 ECLM Page (8 - 11)

## Slide 16: What digital protocol is used by APRS?
A. PACTOR
B. 802.11
C. AX.25
D. AMTOR
(C) E2D07 ECLM Page (8 - 11)

## Slide 17: What type of packet frame is used to transmit APRS beacon data?
A. Unnumbered Information
B. Disconnect
C. Acknowledgement
D. Connect
E2D08 ECLM Page (8 - 12)

## Slide 18: What type of packet frame is used to transmit APRS beacon data?
A. Unnumbered Information
B. Disconnect
C. Acknowledgement
D. Connect
(A) E2D08 ECLM Page (8 - 12)

## Slide 19: What type of modulation is used for JT65 contacts?
A. Multi-tone AFSK
B. PSK
C. RTTY
D. IEEE 802.11
E2D09 ECLM Page (8 - 13)

## Slide 20: What type of modulation is used for JT65 contacts?
A. Multi-tone AFSK
B. PSK
C. RTTY
D. IEEE 802.11
(A) E2D09 ECLM Page (8 - 13)

## Slide 21: How can an APRS station be used to help support a public service communications activity?
A. An APRS station with an emergency medical technician can automatically transmit medical data to the nearest hospital
B. APRS stations with General Personnel Scanners can automatically relay the participant numbers and time as they pass the check points
C. An APRS station with a Global Positioning System unit can automatically transmit information to show a mobile station's position during the event
D. All these choices are correct
E2D10 ECLM Page (8 - 12)

## Slide 22: How can an APRS station be used to help support a public service communications activity?
A. An APRS station with an emergency medical technician can automatically transmit medical data to the nearest hospital
B. APRS stations with General Personnel Scanners can automatically relay the participant numbers and time as they pass the check points
C. An APRS station with a Global Positioning System unit can automatically transmit information to show a mobile station's position during the event
D. All these choices are correct
(C) E2D10 ECLM Page (8 - 12)

## Slide 23: Which of the following data are used by the APRS network to communicate station location?
A. Polar coordinates
B. Time and frequency
C. Radio direction finding spectrum analysis
D. Latitude and longitude
E2D11 ECLM Page (8 - 12)

## Slide 24: Which of the following data are used by the APRS network to communicate station location?
A. Polar coordinates
B. Time and frequency
C. Radio direction finding spectrum analysis
D. Latitude and longitude
(D) E2D11 ECLM Page (8 - 12)

## Slide 25: Which of the following types of modulation is common for data emissions below 30 MHz?
A. DTMF tones modulating an FM signal
B. FSK
C. Pulse modulation
D. Spread spectrum
E2E01 ECLM Page (8 - 10)

## Slide 26: Which of the following types of modulation is common for data emissions below 30 MHz?
A. DTMF tones modulating an FM signal
B. FSK
C. Pulse modulation
D. Spread spectrum
(B) E2E01 ECLM Page (8 - 10)

## Slide 27: What do the letters FEC mean as they relate to digital operation?
A. Forward Error Correction
B. First Error Correction
C. Fatal Error Correction
D. Final Error Correction
E2E02 ECLM Page (8 - 17)

## Slide 28: What do the letters FEC mean as they relate to digital operation?
A. Forward Error Correction
B. First Error Correction
C. Fatal Error Correction
D. Final Error Correction
(A) E2E02 ECLM Page (8 - 17)

## Slide 29: How is the timing of FT4 contacts organized?
A. By exchanging ACK/NAK packets
B. Stations take turns on alternate days
C. Alternating transmissions at 7.5 second intervals
D. It depends on the lunar phase
E2E03 ECLM Page (8 - 13)

## Slide 30: How is the timing of FT4 contacts organized?
A. By exchanging ACK/NAK packets
B. Stations take turns on alternate days
C. Alternating transmissions at 7.5 second intervals
D. It depends on the lunar phase
(C) E2E03 ECLM Page (8 - 13)

## Slide 31: What is indicated when one of the ellipses in an FSK crossed-ellipse display suddenly disappears?
A. Selective fading has occurred
B. One of the signal filters is saturated
C. The receiver has drifted 5 kHz from the desired receive frequency
D. The mark and space signal have been inverted
E2E04 ECLM Page (8 - 10)

## Slide 32: What is indicated when one of the ellipses in an FSK crossed-ellipse display suddenly disappears?
A. Selective fading has occurred
B. One of the signal filters is saturated
C. The receiver has drifted 5 kHz from the desired receive frequency
D. The mark and space signal have been inverted
(A) E2E04 ECLM Page (8 - 10)

## Slide 33: Which of these digital modes does not support keyboard-to-keyboard operation?
A. PACTOR
B. RTTY
C. PSK31
D. MFSK
E2E05 ECLM Page (8 - 12)

## Slide 34: Which of these digital modes does not support keyboard-to-keyboard operation?
A. PACTOR
B. RTTY
C. PSK31
D. MFSK
(A) E2E05 ECLM Page (8 - 12)

## Slide 35: What is the most common data rate used for HF packet?
A. 48 baud
B. 110 baud
C. 300 baud
D. 1200 baud
E2E06 ECLM Page (8 - 12)

## Slide 36: What is the most common data rate used for HF packet?
A. 48 baud
B. 110 baud
C. 300 baud
D. 1200 baud
(C) E2E06 ECLM Page (8 - 12)

## Slide 37: Which of the following is a possible reason that attempts to initiate contact with a digital station on a clear frequency are unsuccessful?
A. Your transmit frequency is incorrect
B. The protocol version you are using is not supported by the digital station
C. Another station you are unable to hear is using the frequency
D. All these choices are correct
E2E07 ECLM Page (8 - 14)

## Slide 38: Which of the following is a possible reason that attempts to initiate contact with a digital station on a clear frequency are unsuccessful?
A. Your transmit frequency is incorrect
B. The protocol version you are using is not supported by the digital station
C. Another station you are unable to hear is using the frequency
D. All these choices are correct
(D) E2E07 ECLM Page (8 - 14)

## Slide 39: Which of the following HF digital modes can be used to transfer binary files?
A. Hellschreiber
B. PACTOR
C. RTTY
D. AMTOR
E2E08 ECLM Page (8 - 12)

## Slide 40: Which of the following HF digital modes can be used to transfer binary files?
A. Hellschreiber
B. PACTOR
C. RTTY
D. AMTOR
(B) E2E08 ECLM Page (8 - 12)

## Slide 41: Which of the following HF digital modes uses variable-length coding for bandwidth efficiency?
A. RTTY
B. PACTOR
C. MT63
D. PSK31
E2E09 ECLM Page (8 - 7)

## Slide 42: Which of the following HF digital modes uses variable-length coding for bandwidth efficiency?
A. RTTY
B. PACTOR
C. MT63
D. PSK31
(D) E2E09 ECLM Page (8 - 7)

## Slide 43: Which of these digital modes has the narrowest bandwidth?
A. MFSK16
B. 170-Hz shift, 45-baud RTTY
C. PSK31
D. 300-baud packet
E2E10 ECLM Page (8 - 11)

## Slide 44: Which of these digital modes has the narrowest bandwidth?
A. MFSK16
B. 170-Hz shift, 45-baud RTTY
C. PSK31
D. 300-baud packet
(C) E2E10 ECLM Page (8 - 11)

## Slide 45: What is the difference between direct FSK and audio FSK?
A. Direct FSK applies the data signal to the transmitter VFO, while AFSK transmits tones via phone
B. Direct FSK occupies less bandwidth
C. Direct FSK can transmit faster baud rates
D. Only direct FSK can be decoded by computer
E2E11 ECLM Page (8 - 10)

## Slide 46: What is the difference between direct FSK and audio FSK?
A. Direct FSK applies the data signal to the transmitter VFO, while AFSK transmits tones via phone
B. Direct FSK occupies less bandwidth
C. Direct FSK can transmit faster baud rates
D. Only direct FSK can be decoded by computer
(A ) E2E11 ECLM Page (8 - 10)

## Slide 47: How do ALE stations establish contact?
A. ALE constantly scans a list of frequencies, activating the radio when the designated call sign is received
B. ALE radios monitor an internet site for the frequency they are being paged on
C. ALE radios send a constant tone code to establish a frequency for future use
D. ALE radios activate when they hear their signal echoed by back scatter
E2E12 ECLM Page (8 - 6)

## Slide 48: How do ALE stations establish contact?
A. ALE constantly scans a list of frequencies, activating the radio when the designated call sign is received
B. ALE radios monitor an internet site for the frequency they are being paged on
C. ALE radios send a constant tone code to establish a frequency for future use
D. ALE radios activate when they hear their signal echoed by back scatter
(A) E2E12 ECLM Page (8 - 6)

## Slide 49: Which of these digital modes has the fastest data throughput under clear communication conditions?
A. AMTOR
B. 170 Hz shift, 45 baud RTTY
C. PSK31
D. 300 baud packet
E2E13 ECLM Page (8 - 12)

## Slide 50: Which of these digital modes has the fastest data throughput under clear communication conditions?
A. AMTOR
B. 170 Hz shift, 45 baud RTTY
C. PSK31
D. 300 baud packet
(D) E2E13 ECLM Page (8 - 12)