## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is the approximate maximum separation measured along the surface of the Earth between two stations communicating by EME?
A. 500 miles, if the moon is at perigee
B. 2000 miles, if the moon is at apogee
C. 5000 miles, if the moon is at perigee
D. 12,000 miles, if the moon is visible by both stations
E3A01 ECLM Page (10 - 17)

## Slide 4: What is the approximate maximum separation measured along the surface of the Earth between two stations communicating by EME?
A. 500 miles, if the moon is at perigee
B. 2000 miles, if the moon is at apogee
C. 5000 miles, if the moon is at perigee
D. 12,000 miles, if the moon is visible by both stations
(D) E3A01 ECLM Page (10 - 17)

## Slide 5: What characterizes libration fading of an EME signal?
A. A slow change in the pitch of the CW signal
B. A fluttery irregular fading
C. A gradual loss of signal as the sun rises
D. The returning echo is several hertz lower in frequency than the transmitted signal
E3A02 ECLM Page (10 - 17)

## Slide 6: What characterizes libration fading of an EME signal?
A. A slow change in the pitch of the CW signal
B. A fluttery irregular fading
C. A gradual loss of signal as the sun rises
D. The returning echo is several hertz lower in frequency than the transmitted signal
(B) E3A02 ECLM Page (10 - 17)

## Slide 7: When scheduling EME contacts, which of these conditions will generally result in the least path loss?
A. When the moon is at perigee
B. When the moon is full
C. When the moon is at apogee
D. When the MUF is above 30 MHz
E3A03 ECLM Page (10 - 17)

## Slide 8: When scheduling EME contacts, which of these conditions will generally result in the least path loss?
A. When the moon is at perigee
B. When the moon is full
C. When the moon is at apogee
D. When the MUF is above 30 MHz
(A) E3A03 ECLM Page (10 - 17)

## Slide 9: What do Hepburn maps predict?
A. Sporadic E propagation
B. Locations of auroral reflecting zones
C. Likelihood of rain scatter along cold or warm fronts
D. Probability of tropospheric propagation
E3A04 ECLM Page (10 - 12)

## Slide 10: What do Hepburn maps predict?
A. Sporadic E propagation
B. Locations of auroral reflecting zones
C. Likelihood of rain scatter along cold or warm fronts
D. Probability of tropospheric propagation
(D) E3A04 ECLM Page (10 - 12)

## Slide 11: Tropospheric propagation of microwave signals often occurs in association with what phenomenon?
A. Grayline
B. Lightning discharges
C. Warm and cold fronts
D. Sprites and jets
E3A05 ECLM Page (10 - 12)

## Slide 12: Tropospheric propagation of microwave signals often occurs in association with what phenomenon?
A. Grayline
B. Lightning discharges
C. Warm and cold fronts
D. Sprites and jets
(C) E3A05 ECLM Page (10 - 12)

## Slide 13: What might help to restore contact when DX signals become too weak to copy across an entire HF band a few hours after sunset?
A. Switch to a higher frequency HF band
B. Switch to a lower frequency HF band
C. Wait 90 minutes or so for the signal degradation to pass
D. Wait 24 hours before attempting another communication on the band
E3A06 ECLM Page (10 - 7)

## Slide 14: What might help to restore contact when DX signals become too weak to copy across an entire HF band a few hours after sunset?
A. Switch to a higher frequency HF band
B. Switch to a lower frequency HF band
C. Wait 90 minutes or so for the signal degradation to pass
D. Wait 24 hours before attempting another communication on the band
(B) E3A06 ECLM Page (10 - 7)

## Slide 15: Atmospheric ducts capable of propagating microwave signals often form over what geographic feature?
A. Mountain ranges
B. Forests
C. Bodies of water
D. Urban areas
E3A07 ECLM Page (10 - 12)

## Slide 16: Atmospheric ducts capable of propagating microwave signals often form over what geographic feature?
A. Mountain ranges
B. Forests
C. Bodies of water
D. Urban areas
(C) E3A07 ECLM Page (10 - 12)

## Slide 17: When a meteor strikes the Earth's atmosphere, a cylindrical region of free electrons is formed at what layer of the ionosphere?
A. The E layer
B. The F1 layer
C. The F2 layer
D. The D layer
E3A08 ECLM Page (10 - 16)

## Slide 18: When a meteor strikes the Earth's atmosphere, a cylindrical region of free electrons is formed at what layer of the ionosphere?
A. The E layer
B. The F1 layer
C. The F2 layer
D. The D layer
(A) E3A08 ECLM Page (10 - 16)

## Slide 19: Which of the following frequency ranges is most suited for meteor-scatter communications?
A. 1.8 MHz - 1.9 MHz
B. 10 MHz - 14 MHz
C. 28 MHz - 148 MHz
D. 220 MHz - 450 MHz
E3A09 ECLM Page (10 - 16)

## Slide 20: Which of the following frequency ranges is most suited for meteor-scatter communications?
A. 1.8 MHz - 1.9 MHz
B. 10 MHz - 14 MHz
C. 28 MHz - 148 MHz
D. 220 MHz - 450 MHz
(C) E3A09 ECLM Page (10 - 16)

## Slide 21: Which type of atmospheric structure can create a path for microwave propagation?
A. The jet stream
B. Temperature inversion
C. Wind shear
D. Dust devil
E3A10 ECLM Page (10 - 12)

## Slide 22: Which type of atmospheric structure can create a path for microwave propagation?
A. The jet stream
B. Temperature inversion
C. Wind shear
D. Dust devil
(B) E3A10 ECLM Page (10 - 12)

## Slide 23: What is a typical range for tropospheric propagation of microwave signals?
A. 10 miles to 50 miles
B. 100 miles to 300 miles
C. 1200 miles
D. 2500 miles
E3A11 ECLM Page (10 - 12)

## Slide 24: What is a typical range for tropospheric propagation of microwave signals?
A. 10 miles to 50 miles
B. 100 miles to 300 miles
C. 1200 miles
D. 2500 miles
(B) E3A11 ECLM Page (10 - 12)

## Slide 25: What is the cause of auroral activity?
A. The interaction in the F2 layer between the solar wind and the Van Allen belt
B. An extreme low-pressure area in the polar regions
C. The interaction in the E layer of charged particles from the Sun with the Earth’s magnetic field
D. Meteor showers concentrated in the extreme northern and southern latitudes
E3A12 ECLM Page (10 - 14)

## Slide 26: What is the cause of auroral activity?
A. The interaction in the F2 layer between the solar wind and the Van Allen belt
B. An extreme low-pressure area in the polar regions
C. The interaction in the E layer of charged particles from the Sun with the Earth’s magnetic field
D. Meteor showers concentrated in the extreme northern and southern latitudes
(C) E3A12 ECLM Page (10 - 14)

## Slide 27: Which of these emission modes is best for auroral propagation?
A. CW
B. SSB
C. FM
D. RTTY
E3A13 ECLM Page (10 - 14)

## Slide 28: Which of these emission modes is best for auroral propagation?
A. CW
B. SSB
C. FM
D. RTTY
(A) E3A13 ECLM Page (10 - 14)

## Slide 29: What is meant by circularly polarized electromagnetic waves?
A. Waves with an electric field bent into a circular shape
B. Waves with a rotating electric field
C. Waves that circle the Earth
D. Waves produced by a loop antenna
E3A14 ECLM Page (10 - 3)

## Slide 30: What is meant by circularly polarized electromagnetic waves?
A. Waves with an electric field bent into a circular shape
B. Waves with a rotating electric field
C. Waves that circle the Earth
D. Waves produced by a loop antenna
(B) E3A14 ECLM Page (10 - 3)

## Slide 31: What is transequatorial propagation?
A. Propagation between two mid-latitude points at approximately the same distance north and south of the magnetic equator
B. Propagation between points located on the magnetic equator
C. Propagation between a point on the equator and its antipodal point
D. Propagation between points at the same latitude
E3B01 ECLM Page (10 - 13)

## Slide 32: What is transequatorial propagation?
A. Propagation between two mid-latitude points at approximately the same distance north and south of the magnetic equator
B. Propagation between points located on the magnetic equator
C. Propagation between a point on the equator and its antipodal point
D. Propagation between points at the same latitude
(A) E3B01 ECLM Page (10 - 13)

## Slide 33: What is the approximate maximum range for signals using transequatorial propagation?
A. 1000 miles
B. 2500 miles
C. 5000 miles
D. 7500 miles
E3B02 ECLM Page (10 - 14)

## Slide 34: What is the approximate maximum range for signals using transequatorial propagation?
A. 1000 miles
B. 2500 miles
C. 5000 miles
D. 7500 miles
(C) E3B02 ECLM Page (10 - 14)

## Slide 35: What is the best time of day for transequatorial propagation?
A. Morning
B. Noon
C. Afternoon or early evening
D. Late at night
E3B03 ECLM Page (10 - 14)

## Slide 36: What is the best time of day for transequatorial propagation?
A. Morning
B. Noon
C. Afternoon or early evening
D. Late at night
(C) E3B03 ECLM Page (10 - 14)

## Slide 37: What is meant by the terms "extraordinary" and "ordinary" waves?
A. Extraordinary waves describe rare long skip propagation compared to ordinary waves which travel shorter distances
B. Independent waves created in the ionosphere that are elliptically polarized
C. Long path and short path waves
D. Refracted rays and reflected waves
E3B04 ECLM Page (10 - 7)

## Slide 38: What is meant by the terms "extraordinary" and "ordinary" waves?
A. Extraordinary waves describe rare long skip propagation compared to ordinary waves which travel shorter distances
B. Independent waves created in the ionosphere that are elliptically polarized
C. Long path and short path waves
D. Refracted rays and reflected waves
(B) E3B04 ECLM Page (10 - 7)

## Slide 39: Which amateur bands typically support long-path propagation?
A. Only 160 meters to 40 meters
B. Only 30 meters to 10 meters
C. 160 meters to 10 meters
D. 6 meters to 2 meters
E3B05 ECLM Page (10 - 9)

## Slide 40: Which amateur bands typically support long-path propagation?
A. Only 160 meters to 40 meters
B. Only 30 meters to 10 meters
C. 160 meters to 10 meters
D. 6 meters to 2 meters
(C) E3B05 ECLM Page (10 - 9)

## Slide 41: Which of the following amateur bands most frequently provides long-path propagation?
A. 80 meters
B. 20 meters
C. 10 meters
D. 6 meters
E3B06 ECLM Page (10 - 9)

## Slide 42: Which of the following amateur bands most frequently provides long-path propagation?
A. 80 meters
B. 20 meters
C. 10 meters
D. 6 meters
(B) E3B06 ECLM Page (10 - 9)

## Slide 43: What happens to linearly polarized radio waves that split into ordinary and extraordinary waves in the ionosphere?
A. They are bent toward the magnetic poles
B. They become depolarized
C. They become elliptically polarized
D. They become phase-locked
E3B07 ECLM Page (10 - 7)

## Slide 44: What happens to linearly polarized radio waves that split into ordinary and extraordinary waves in the ionosphere?
A. They are bent toward the magnetic poles
B. They become depolarized
C. They become elliptically polarized
D. They become phase-locked
(C) E3B07 ECLM Page (10 - 7)

## Slide 45: E3B08 - The question has been withdrawn.

## Slide 46: At what time of year is sporadic E propagation most likely to occur?
A. Around the solstices, especially the summer solstice
B. Around the solstices, especially the winter solstice
C. Around the equinoxes, especially the spring equinox
D. Around the equinoxes, especially the fall equinox
E3B09 ECLM Page (10 - 13)

## Slide 47: At what time of year is sporadic E propagation most likely to occur?
A. Around the solstices, especially the summer solstice
B. Around the solstices, especially the winter solstice
C. Around the equinoxes, especially the spring equinox
D. Around the equinoxes, especially the fall equinox
(A) E3B09 ECLM Page (10 - 13)

## Slide 48: Why is chordal hop propagation desirable?
A. The signal experiences less loss compared to multi-hop using Earth as a reflector
B. The MUF for chordal hop propagation is much lower than for normal skip propagation
C. Atmospheric noise is lower in the direction of chordal hop propagation
D. Signals travel faster along ionospheric chords
E3B10 ECLM Page (10 - 6)

## Slide 49: Why is chordal hop propagation desirable?
A. The signal experiences less loss compared to multi-hop using Earth as a reflector
B. The MUF for chordal hop propagation is much lower than for normal skip propagation
C. Atmospheric noise is lower in the direction of chordal hop propagation
D. Signals travel faster along ionospheric chords
(A) E3B10 ECLM Page (10 - 6)

## Slide 50: At what time of day can sporadic E propagation occur?
A. Only around sunset
B. Only around sunset and sunrise
C. Only in hours of darkness
D. Any time
E3B11 ECLM Page (10 - 13)

## Slide 51: At what time of day can sporadic E propagation occur?
A. Only around sunset
B. Only around sunset and sunrise
C. Only in hours of darkness
D. Any time
(D) E3B11 ECLM Page (10 - 13)

## Slide 52: What is the primary characteristic of chordal hop propagation?
A. Propagation away from the great circle bearing between stations
B. Successive ionospheric refractions without an intermediate reflection from the ground
C. Propagation across the geomagnetic equator
D. Signals reflected back toward the transmitting station
E3B12 ECLM Page (10 - 6)

## Slide 53: What is the primary characteristic of chordal hop propagation?
A. Propagation away from the great circle bearing between stations
B. Successive ionospheric refractions without an intermediate reflection from the ground
C. Propagation across the geomagnetic equator
D. Signals reflected back toward the transmitting station
(B) E3B12 ECLM Page (10 - 6)

## Slide 54: What does the radio communication term “ray tracing” describe?
A. The process in which an electronic display presents a pattern
B. Modeling a radio wave's path through the ionosphere
C. Determining the radiation pattern from an array of antennas
D. Evaluating high voltage sources for x-rays
E3C01 ECLM Page (10 - 8)

## Slide 55: What does the radio communication term “ray tracing” describe?
A. The process in which an electronic display presents a pattern
B. Modeling a radio wave's path through the ionosphere
C. Determining the radiation pattern from an array of antennas
D. Evaluating high voltage sources for x-rays
(B) E3C01 ECLM Page (10 - 8)

## Slide 56: What is indicated by a rising A or K index?
A. Increasing disruption of the geomagnetic field
B. Decreasing disruption of the geomagnetic field
C. Higher levels of solar UV radiation
D. An increase in the critical frequency
E3C02 ECLM Page (10 - 5)

## Slide 57: What is indicated by a rising A or K index?
A. Increasing disruption of the geomagnetic field
B. Decreasing disruption of the geomagnetic field
C. Higher levels of solar UV radiation
D. An increase in the critical frequency
(A) E3C02 ECLM Page (10 - 5)

## Slide 58: Which of the following signal paths is most likely to experience high levels of absorption when the A index or K index is elevated?
A. Transequatorial
B. Polar
C. Sporadic E
D. NVIS
E3C03 ECLM Page (10 - 8)

## Slide 59: Which of the following signal paths is most likely to experience high levels of absorption when the A index or K index is elevated?
A. Transequatorial
B. Polar
C. Sporadic E
D. NVIS
(B) E3C03 ECLM Page (10 - 8)

## Slide 60: What does the value of Bz (B sub Z) represent?
A. Geomagnetic field stability
B. Critical frequency for vertical transmissions
C. Direction and strength of the interplanetary magnetic field
D. Duration of long-delayed echoes
E3C04 ECLM Page (10 - 5)

## Slide 61: What does the value of Bz (B sub Z) represent?
A. Geomagnetic field stability
B. Critical frequency for vertical transmissions
C. Direction and strength of the interplanetary magnetic field
D. Duration of long-delayed echoes
(C) E3C04 ECLM Page (10 - 5)

## Slide 62: What orientation of Bz (B sub z) increases the likelihood that incoming particles from the sun will cause disturbed conditions?
A. Southward
B. Northward
C. Eastward
D. Westward
E3C05 ECLM Page (10 - 5)

## Slide 63: What orientation of Bz (B sub z) increases the likelihood that incoming particles from the sun will cause disturbed conditions?
A. Southward
B. Northward
C. Eastward
D. Westward
(A) E3C05 ECLM Page (10 - 5)

## Slide 64: By how much does the VHF/UHF radio horizon distance exceed the geometric horizon?
A. By approximately 15 percent of the distance
B. By approximately twice the distance
C. By approximately 50 percent of the distance
D. By approximately four times the distance
E3C06 ECLM Page (10 - 10)

## Slide 65: By how much does the VHF/UHF radio horizon distance exceed the geometric horizon?
A. By approximately 15 percent of the distance
B. By approximately twice the distance
C. By approximately 50 percent of the distance
D. By approximately four times the distance
(A) E3C06 ECLM Page (10 - 10)

## Slide 66: Which of the following descriptors indicates the greatest solar flare intensity?
A. Class A
B. Class B
C. Class M
D. Class X
E3C07 ECLM Page (10 - 4)

## Slide 67: Which of the following descriptors indicates the greatest solar flare intensity?
A. Class A
B. Class B
C. Class M
D. Class X
(D) E3C07 ECLM Page (10 - 4)

## Slide 68: What does the space weather term "G5" mean?
A. An extreme geomagnetic storm
B. Very low solar activity
C. Moderate solar wind
D. Waning sunspot numbers
E3C08 ECLM Page (10 - 5)

## Slide 69: What does the space weather term "G5" mean?
A. An extreme geomagnetic storm
B. Very low solar activity
C. Moderate solar wind
D. Waning sunspot numbers
(A) E3C08 ECLM Page (10 - 5)

## Slide 70: How does the intensity of an X3 flare compare to that of an X2 flare?
A. 10 percent greater
B. 50 percent greater
C. Twice as great
D. Four times as great
E3C09 ECLM Page (10 - 4)

## Slide 71: How does the intensity of an X3 flare compare to that of an X2 flare?
A. 10 percent greater
B. 50 percent greater
C. Twice as great
D. Four times as great
(B) E3C09 ECLM Page (10 - 4)

## Slide 72: What does the 304A solar parameter measure?
A. The ratio of x-ray flux to radio flux, correlated to sunspot number
B. UV emissions at 304 angstroms, correlated to the solar flux index
C. The solar wind velocity at 304 degrees from the solar equator, correlated to solar activity
D. The solar emission at 304 GHz, correlated to x-ray flare levels
E3C10 ECLM Page (10 - 4)

## Slide 73: What does the 304A solar parameter measure?
A. The ratio of x-ray flux to radio flux, correlated to sunspot number
B. UV emissions at 304 angstroms, correlated to the solar flux index
C. The solar wind velocity at 304 degrees from the solar equator, correlated to solar activity
D. The solar emission at 304 GHz, correlated to x-ray flare levels
(B) E3C10 ECLM Page (10 - 4)

## Slide 74: What does VOACAP software model?
A. AC voltage and impedance
B. VHF radio propagation
C. HF propagation
D. AC current and impedance
E3C11 ECLM Page (10 - 8)

## Slide 75: What does VOACAP software model?
A. AC voltage and impedance
B. VHF radio propagation
C. HF propagation
D. AC current and impedance
(C) E3C11 ECLM Page (10 - 8)

## Slide 76: How does the maximum range of ground-wave propagation change when the signal frequency is increased?
A. It stays the same
B. It increases
C. It decreases
D. It peaks at roughly 14 MHz
E3C12 ECLM Page (10 - 6)

## Slide 77: How does the maximum range of ground-wave propagation change when the signal frequency is increased?
A. It stays the same
B. It increases
C. It decreases
D. It peaks at roughly 14 MHz
(C) E3C12 ECLM Page (10 - 6)

## Slide 78: What type of polarization is best for ground-wave propagation?
A. Vertical
B. Horizontal
C. Circular
D. Elliptical
E3C13 ECLM Page (10 - 6)

## Slide 79: What type of polarization is best for ground-wave propagation?
A. Vertical
B. Horizontal
C. Circular
D. Elliptical
(A) E3C13 ECLM Page (10 - 6)

## Slide 80: Why does the radio-path horizon distance exceed the geometric horizon?
A. E-region skip
B. D-region skip
C. Due to the Doppler effect
D. Downward bending due to density variations in the atmosphere
E3C14 ECLM Page (10 - 10)

## Slide 81: Why does the radio-path horizon distance exceed the geometric horizon?
A. E-region skip
B. D-region skip
C. Due to the Doppler effect
D. Downward bending due to density variations in the atmosphere
(D) E3C14 ECLM Page (10 - 10)

## Slide 82: What might be indicated by a sudden rise in radio background noise across a large portion of the HF spectrum?
A. A temperature inversion has occurred
B. A solar flare has occurred
C. Increased transequatorial propagation is likely
D. Long-path propagation is likely
E3C15 ECLM Page (10 - 8)

## Slide 83: What might be indicated by a sudden rise in radio background noise across a large portion of the HF spectrum?
A. A temperature inversion has occurred
B. A solar flare has occurred
C. Increased transequatorial propagation is likely
D. Long-path propagation is likely
(B) E3C15 ECLM Page (10 - 8)