## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is meant by the blocking dynamic range of a receiver?
A. The difference in dB between the noise floor and the level of an incoming signal that will cause 1 dB of gain compression
B. The minimum difference in dB between the levels of two FM signals that will cause one signal to block the other
C. The difference in dB between the noise floor and the third order intercept point
D. The minimum difference in dB between two signals which produce third order intermodulation products greater than the noise floor
E4D01 ECLM Page (7 - 20)

## Slide 4: What is meant by the blocking dynamic range of a receiver?
A. The difference in dB between the noise floor and the level of an incoming signal that will cause 1 dB of gain compression
B. The minimum difference in dB between the levels of two FM signals that will cause one signal to block the other
C. The difference in dB between the noise floor and the third order intercept point
D. The minimum difference in dB between two signals which produce third order intermodulation products greater than the noise floor
(A) E4D01 ECLM Page (7 - 20)

## Slide 5: Which of the following describes problems caused by poor dynamic range in a receiver?
A. Spurious signals caused by cross-modulation and desensitization from strong adjacent signals
B. Oscillator instability requiring frequent retuning and loss of ability to recover the opposite sideband
C. Cross-modulation of the desired signal and insufficient audio power to operate the speaker
D. Oscillator instability and severe audio distortion of all but the strongest received signals
E4D02 ECLM Page (7 - 22)

## Slide 6: Which of the following describes problems caused by poor dynamic range in a receiver?
A. Spurious signals caused by cross-modulation and desensitization from strong adjacent signals
B. Oscillator instability requiring frequent retuning and loss of ability to recover the opposite sideband
C. Cross-modulation of the desired signal and insufficient audio power to operate the speaker
D. Oscillator instability and severe audio distortion of all but the strongest received signals
(A) E4D02 ECLM Page (7 - 22)

## Slide 7: How can intermodulation interference between two repeaters occur?
A. When the repeaters are in close proximity and the signals cause feedback in the final amplifier of one or both transmitters
B. When the repeaters are in close proximity and the signals mix in the final amplifier of one or both transmitters
C. When the signals from the transmitters are reflected out of phase from airplanes passing overhead
D. When the signals from the transmitters are reflected in phase from airplanes passing overhead
E4D03 ECLM Page (7 - 22)

## Slide 8: How can intermodulation interference between two repeaters occur?
A. When the repeaters are in close proximity and the signals cause feedback in the final amplifier of one or both transmitters
B. When the repeaters are in close proximity and the signals mix in the final amplifier of one or both transmitters
C. When the signals from the transmitters are reflected out of phase from airplanes passing overhead
D. When the signals from the transmitters are reflected in phase from airplanes passing overhead
(B) E4D03 ECLM Page (7 - 22)

## Slide 9: Which of the following may reduce or eliminate intermodulation interference in a repeater caused by another transmitter operating in close proximity?
A. A band-pass filter in the feed line between the transmitter and receiver
B. A properly terminated circulator at the output of the repeater's transmitter
C. Utilizing a Class C final amplifier
D. Utilizing a Class D final amplifier
E4D04 ECLM Page (7 - 22)

## Slide 10: Which of the following may reduce or eliminate intermodulation interference in a repeater caused by another transmitter operating in close proximity?
A. A band-pass filter in the feed line between the transmitter and receiver
B. A properly terminated circulator at the output of the repeater's transmitter
C. Utilizing a Class C final amplifier
D. Utilizing a Class D final amplifier
(B) E4D04 ECLM Page (7 - 22)

## Slide 11: What transmitter frequencies would cause an intermodulation-product signal in a receiver tuned to 146.70 MHz when a nearby station transmits on 146.52 MHz?
A. 146.34 MHz and 146.61 MHz
B. 146.88 MHz and 146.34 MHz
C. 146.10 MHz and 147.30 MHz
D. 173.35 MHz and 139.40 MHz
E4D05 ECLM Page (7 - 18)

## Slide 12: What transmitter frequencies would cause an intermodulation-product signal in a receiver tuned to 146.70 MHz when a nearby station transmits on 146.52 MHz?
A. 146.34 MHz and 146.61 MHz
B. 146.88 MHz and 146.34 MHz
C. 146.10 MHz and 147.30 MHz
D. 173.35 MHz and 139.40 MHz
(A) E4D05 ECLM Page (7 - 18)

## Slide 13: What is the term for spurious signals generated by the combination of two or more signals in a non-linear device or circuit?
A. Amplifier desensitization
B. Neutralization
C. Adjacent channel interference
D. Intermodulation
E4D06 ECLM Page (7 - 22)

## Slide 14: What is the term for spurious signals generated by the combination of two or more signals in a non-linear device or circuit?
A. Amplifier desensitization
B. Neutralization
C. Adjacent channel interference
D. Intermodulation
(D ) E4D06 ECLM Page (7 - 22)

## Slide 15: Which of the following reduces the likelihood of receiver desensitization?
A. Decrease the RF bandwidth of the receiver
B. Raise the receiver IF frequency
C. Increase the receiver front end gain
D. Switch from fast AGC to slow AGC
E4D07 ECLM Page (7 - 17)

## Slide 16: Which of the following reduces the likelihood of receiver desensitization?
A. Decrease the RF bandwidth of the receiver
B. Raise the receiver IF frequency
C. Increase the receiver front end gain
D. Switch from fast AGC to slow AGC
(A) E4D07 ECLM Page (7 - 17)

## Slide 17: What causes intermodulation in an electronic circuit?
A. Too little gain
B. Lack of neutralization
C. Nonlinear circuits or devices
D. Positive feedback
E4D08 ECLM Page (7 - 22)

## Slide 18: What causes intermodulation in an electronic circuit?
A. Too little gain
B. Lack of neutralization
C. Nonlinear circuits or devices
D. Positive feedback
(C) E4D08 ECLM Page (7 - 22)

## Slide 19: What is the purpose of the preselector in a communications receiver?
A. To store often-used frequencies
B. To provide a range of AGC time constants
C. To increase rejection of signals outside the desired band
D. To allow selection of the optimum RF amplifier device
E4D09 ECLM Page (7 - 14)

## Slide 20: What is the purpose of the preselector in a communications receiver?
A. To store often-used frequencies
B. To provide a range of AGC time constants
C. To increase rejection of signals outside the desired band
D. To allow selection of the optimum RF amplifier device
(C) E4D09 ECLM Page (7 - 14)

## Slide 21: What does a third-order intercept level of 40 dBm mean with respect to receiver performance?
A. Signals less than 40 dBm will not generate audible third-order intermodulation products
B. The receiver can tolerate signals up to 40 dB above the noise floor without producing third-order intermodulation products
C. A pair of 40 dBm input signals will theoretically generate a third-order intermodulation product that has the same output amplitude as either of the input signals
D. A pair of 1 mW input signals will produce a third-order intermodulation product that is 40 dB stronger than the input signal
E4D10 ECLM Page (7 - 19)

## Slide 22: What does a third-order intercept level of 40 dBm mean with respect to receiver performance?
A. Signals less than 40 dBm will not generate audible third-order intermodulation products
B. The receiver can tolerate signals up to 40 dB above the noise floor without producing third-order intermodulation products
C. A pair of 40 dBm input signals will theoretically generate a third-order intermodulation product that has the same output amplitude as either of the input signals
D. A pair of 1 mW input signals will produce a third-order intermodulation product that is 40 dB stronger than the input signal
(C) E4D10 ECLM Page (7 - 19)

## Slide 23: Why are odd-order intermodulation products, created within a receiver, of particular interest compared to other products?
A. Odd-order products of two signals in the band of interest are also likely to be within the band
B. Odd-order products overload the IF filters
C. Odd-order products are an indication of poor image rejection
D. Odd-order intermodulation produces three products for every input signal within the band of interest
E4D11 ECLM Page (7 - 18)

## Slide 24: Why are odd-order intermodulation products, created within a receiver, of particular interest compared to other products?
A. Odd-order products of two signals in the band of interest are also likely to be within the band
B. Odd-order products overload the IF filters
C. Odd-order products are an indication of poor image rejection
D. Odd-order intermodulation produces three products for every input signal within the band of interest
(A) E4D11 ECLM Page (7 - 18)

## Slide 25: What is the term for the reduction in receiver sensitivity caused by a strong signal near the received frequency?
A. Desensitization
B. Quieting
C. Cross-modulation interference
D. Squelch gain rollback
E4D12 ECLM Page (7 - 16)

## Slide 26: What is the term for the reduction in receiver sensitivity caused by a strong signal near the received frequency?
A. Desensitization
B. Quieting
C. Cross-modulation interference
D. Squelch gain rollback
(A) E4D12 ECLM Page (7 - 16)

## Slide 27: What problem can occur when using an automatic notch filter (ANF) to remove interfering carriers while receiving CW signals?
A. Removal of the CW signal as well as the interfering carrier
B. Any nearby signal passing through the DSP system will overwhelm the desired signal
C. Received CW signals will appear to be modulated at the DSP clock frequency
D. Ringing in the DSP filter will completely remove the spaces between the CW characters
E4E01 ECLM Page (7 - 27)

## Slide 28: What problem can occur when using an automatic notch filter (ANF) to remove interfering carriers while receiving CW signals?
A. Removal of the CW signal as well as the interfering carrier
B. Any nearby signal passing through the DSP system will overwhelm the desired signal
C. Received CW signals will appear to be modulated at the DSP clock frequency
D. Ringing in the DSP filter will completely remove the spaces between the CW characters
(A) E4E01 ECLM Page (7 - 27)

## Slide 29: Which of the following types of noise can often be reduced with a digital signal processing noise filter?
A. Broadband white noise
B. Ignition noise
C. Power line noise
D. All these choices are correct
E4E02 ECLM Page (7 - 27)

## Slide 30: Which of the following types of noise can often be reduced with a digital signal processing noise filter?
A. Broadband white noise
B. Ignition noise
C. Power line noise
D. All these choices are correct
(D) E4E02 ECLM Page (7 - 27)

## Slide 31: Which of the following signals might a receiver noise blanker be able to remove from desired signals?
A. Signals that are constant at all IF levels
B. Signals that appear across a wide bandwidth
C. Signals that appear at one IF but not another
D. Signals that have a sharply peaked frequency distribution
E4E03 ECLM Page (7 - 26)

## Slide 32: Which of the following signals might a receiver noise blanker be able to remove from desired signals?
A. Signals that are constant at all IF levels
B. Signals that appear across a wide bandwidth
C. Signals that appear at one IF but not another
D. Signals that have a sharply peaked frequency distribution
(B) E4E03 ECLM Page (7 - 26)

## Slide 33: How can conducted and radiated noise caused by an automobile alternator be suppressed?
A. By installing filter capacitors in series with the DC power lead and a blocking capacitor in the field lead
B. By installing a noise suppression resistor and a blocking capacitor in both leads
C. By installing a high-pass filter in series with the radio's power lead and a low-pass filter in parallel with the field lead
D. By connecting the radio's power leads directly to the battery and by installing coaxial capacitors in line with the alternator leads
E4E04 ECLM Page (7 - 26)

## Slide 34: How can conducted and radiated noise caused by an automobile alternator be suppressed?
A. By installing filter capacitors in series with the DC power lead and a blocking capacitor in the field lead
B. By installing a noise suppression resistor and a blocking capacitor in both leads
C. By installing a high-pass filter in series with the radio's power lead and a low-pass filter in parallel with the field lead
D. By connecting the radio's power leads directly to the battery and by installing coaxial capacitors in line with the alternator leads
(D) E4E04 ECLM Page (7 - 26)

## Slide 35: How can radio frequency interference from an AC motor be suppressed?
A. By installing a high-pass filter in series with the motor’s power leads
B. By installing a brute-force AC-line filter in series with the motor leads
C. By installing a bypass capacitor in series with the motor leads
D. By using a ground-fault current interrupter in the circuit used to power the motor
E4E05 ECLM Page (7 - 25)

## Slide 36: How can radio frequency interference from an AC motor be suppressed?
A. By installing a high-pass filter in series with the motor’s power leads
B. By installing a brute-force AC-line filter in series with the motor leads
C. By installing a bypass capacitor in series with the motor leads
D. By using a ground-fault current interrupter in the circuit used to power the motor
(B) E4E05 ECLM Page (7 - 25)

## Slide 37: What is one type of electrical interference that might be caused by a nearby personal computer?
A. A loud AC hum in the audio output of your station receiver
B. A clicking noise at intervals of a few seconds
C. The appearance of unstable modulated or unmodulated signals at specific frequencies
D. A whining type noise that continually pulses off and on
E4E06 ECLM Page (7 - 25)

## Slide 38: What is one type of electrical interference that might be caused by a nearby personal computer?
A. A loud AC hum in the audio output of your station receiver
B. A clicking noise at intervals of a few seconds
C. The appearance of unstable modulated or unmodulated signals at specific frequencies
D. A whining type noise that continually pulses off and on
(C) E4E06 ECLM Page (7 - 25)

## Slide 39: Which of the following can cause shielded cables to radiate or receive interference?
A. Low inductance ground connections at both ends of the shield
B. Common mode currents on the shield and conductors
C. Use of braided shielding material
D. Tying all ground connections to a common point resulting in differential mode currents in the shield
E4E07 ECLM Page (7 - 25)

## Slide 40: Which of the following can cause shielded cables to radiate or receive interference?
A. Low inductance ground connections at both ends of the shield
B. Common mode currents on the shield and conductors
C. Use of braided shielding material
D. Tying all ground connections to a common point resulting in differential mode currents in the shield
(B) E4E07 ECLM Page (7 - 25)

## Slide 41: What current flows equally on all conductors of an unshielded multi-conductor cable?
A. Differential-mode current
B. Common-mode current
C. Reactive current only
D. Return current
E4E08 ECLM Page (7 - 25)

## Slide 42: What current flows equally on all conductors of an unshielded multi-conductor cable?
A. Differential-mode current
B. Common-mode current
C. Reactive current only
D. Return current
(B) E4E08 ECLM Page (7 - 25)

## Slide 43: What undesirable effect can occur when using an IF noise blanker?
A. Received audio in the speech range might have an echo effect
B. The audio frequency bandwidth of the received signal might be compressed
C. Nearby signals may appear to be excessively wide even if they meet emission standards
D. FM signals can no longer be demodulated
E4E09 ECLM Page (7 - 26)

## Slide 44: What undesirable effect can occur when using an IF noise blanker?
A. Received audio in the speech range might have an echo effect
B. The audio frequency bandwidth of the received signal might be compressed
C. Nearby signals may appear to be excessively wide even if they meet emission standards
D. FM signals can no longer be demodulated
(C) E4E09 ECLM Page (7 - 26)

## Slide 45: What might be the cause of a loud roaring or buzzing AC line interference that comes and goes at intervals?
A. Arcing contacts in a thermostatically controlled device
B. A defective doorbell or doorbell transformer inside a nearby residence
C. A malfunctioning illuminated advertising display
D. All these choices are correct
E4E10 ECLM Page (7 - 25)

## Slide 46: What might be the cause of a loud roaring or buzzing AC line interference that comes and goes at intervals?
A. Arcing contacts in a thermostatically controlled device
B. A defective doorbell or doorbell transformer inside a nearby residence
C. A malfunctioning illuminated advertising display
D. All these choices are correct
(D) E4E10 ECLM Page (7 - 25)

## Slide 47: What could cause local AM broadcast band signals to combine to generate spurious signals in the MF or HF bands?
A. One or more of the broadcast stations is transmitting an over-modulated signal
B. Nearby corroded metal joints are mixing and re-radiating the broadcast signals
C. You are receiving skywave signals from a distant station
D. Your station receiver IF amplifier stage is defective
E4E11 ECLM Page (7 - 23)

## Slide 48: What could cause local AM broadcast band signals to combine to generate spurious signals in the MF or HF bands?
A. One or more of the broadcast stations is transmitting an over-modulated signal
B. Nearby corroded metal joints are mixing and re-radiating the broadcast signals
C. You are receiving skywave signals from a distant station
D. Your station receiver IF amplifier stage is defective
(B) E4E11 ECLM Page (7 - 23)