## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: In what application is gallium arsenide used as a semiconductor material?
A. In high-current rectifier circuits
B. In high-power audio circuits
C. In microwave circuits
D. In very low frequency RF circuits
E6A01 ECLM Page (5 - 13)

## Slide 4: In what application is gallium arsenide used as a semiconductor material?
A. In high-current rectifier circuits
B. In high-power audio circuits
C. In microwave circuits
D. In very low frequency RF circuits
(C) E6A01 ECLM Page (5 - 13)

## Slide 5: Which of the following semiconductor materials contains excess free electrons?
A. N-type
B. P-type
C. Bipolar
D. Insulated gate
E6A02 ECLM Page (5 - 2)

## Slide 6: Which of the following semiconductor materials contains excess free electrons?
A. N-type
B. P-type
C. Bipolar
D. Insulated gate
(A) E6A02 ECLM Page (5 - 2)

## Slide 7: Why does a PN-junction diode not conduct current when reverse biased?
A. Only P-type semiconductor material can conduct current
B. Only N-type semiconductor material can conduct current
C. Holes in P-type material and electrons in the N-type material are separated by the applied voltage, widening the depletion region
D. Excess holes in P-type material combine with the electrons in N-type material, converting the entire diode into an insulator
E6A03 ECLM Page (5 - 3)

## Slide 8: Why does a PN-junction diode not conduct current when reverse biased?
A. Only P-type semiconductor material can conduct current
B. Only N-type semiconductor material can conduct current
C. Holes in P-type material and electrons in the N-type material are separated by the applied voltage, widening the depletion region
D. Excess holes in P-type material combine with the electrons in N-type material, converting the entire diode into an insulator
(C) E6A03 ECLM Page (5 - 3)

## Slide 9: What is the name given to an impurity atom that adds holes to a semiconductor crystal structure?
A. Insulator impurity
B. N-type impurity
C. Acceptor impurity
D. Donor impurity
E6A04 ECLM Page (5 - 2)

## Slide 10: What is the name given to an impurity atom that adds holes to a semiconductor crystal structure?
A. Insulator impurity
B. N-type impurity
C. Acceptor impurity
D. Donor impurity
(C) E6A04 ECLM Page (5 - 2)

## Slide 11: How does DC input impedance at the gate of a field-effect transistor compare with the DC input impedance of a bipolar transistor?
A. They are both low impedance
B. An FET has lower input impedance
C. An FET has higher input impedance
D. They are both high impedance
E6A05 ECLM Page (5 - 10)

## Slide 12: How does DC input impedance at the gate of a field-effect transistor compare with the DC input impedance of a bipolar transistor?
A. They are both low impedance
B. An FET has lower input impedance
C. An FET has higher input impedance
D. They are both high impedance
(C) E6A05 ECLM Page (5 - 10)

## Slide 13: What is the beta of a bipolar junction transistor?
A. The frequency at which the current gain is reduced to 0.707
B. The change in collector current with respect to base current
C. The breakdown voltage of the base to collector junction
D. The switching speed
E6A06 ECLM Page (5 - 9)

## Slide 14: What is the beta of a bipolar junction transistor?
A. The frequency at which the current gain is reduced to 0.707
B. The change in collector current with respect to base current
C. The breakdown voltage of the base to collector junction
D. The switching speed
(B) E6A06 ECLM Page (5 - 9)

## Slide 15: Which of the following indicates that a silicon NPN junction transistor is biased on?
A. Base-to-emitter resistance of approximately 6 to 7 ohms
B. Base-to-emitter resistance of approximately 0.6 to 0.7 ohms
C. Base-to-emitter voltage of approximately 6 to 7 volts
D. Base-to-emitter voltage of approximately 0.6 to 0.7 volts
E6A07 ECLM Page (5 - 8)

## Slide 16: Which of the following indicates that a silicon NPN junction transistor is biased on?
A. Base-to-emitter resistance of approximately 6 to 7 ohms
B. Base-to-emitter resistance of approximately 0.6 to 0.7 ohms
C. Base-to-emitter voltage of approximately 6 to 7 volts
D. Base-to-emitter voltage of approximately 0.6 to 0.7 volts
(D) E6A07 ECLM Page (5 - 8)

## Slide 17: What term indicates the frequency at which the grounded-base current gain of a transistor has decreased to 0.7 of the gain obtainable at 1 kHz?
A. Corner frequency
B. Alpha rejection frequency
C. Beta cutoff frequency
D. Alpha cutoff frequency
E6A08 ECLM Page (5 - 9)

## Slide 18: What term indicates the frequency at which the grounded-base current gain of a transistor has decreased to 0.7 of the gain obtainable at 1 kHz?
A. Corner frequency
B. Alpha rejection frequency
C. Beta cutoff frequency
D. Alpha cutoff frequency
(D) E6A08 ECLM Page (5 - 9)

## Slide 19: What is a depletion-mode FET?
A. An FET that exhibits a current flow between source and drain when no gate voltage is applied
B. An FET that has no current flow between source and drain when no gate voltage is applied
C. Any FET without a channel
D. Any FET for which holes are the majority carriers
E6A09 ECLM Page (5 - 11)

## Slide 20: What is a depletion-mode FET?
A. An FET that exhibits a current flow between source and drain when no gate voltage is applied
B. An FET that has no current flow between source and drain when no gate voltage is applied
C. Any FET without a channel
D. Any FET for which holes are the majority carriers
(A) E6A09 ECLM Page (5 - 11)

## Slide 21: In Figure E6-1, what is the schematic symbol for an N-channel dual-gate MOSFET?
A. 2
B. 4
C. 5
D. 6
E6A10 ECLM Page (5 - 11)

## Slide 22: In Figure E6-1, what is the schematic symbol for an N-channel dual-gate MOSFET?
A. 2
B. 4
C. 5
D. 6
(B) E6A10 ECLM Page (5 - 11)

## Slide 23: In Figure E6-1, what is the schematic symbol for a P-channel junction FET?
A. 1
B. 2
C. 3
D. 6
E6A11 ECLM Page (5 - 10)

## Slide 24: In Figure E6-1, what is the schematic symbol for a P-channel junction FET?
A. 1
B. 2
C. 3
D. 6
(A) E6A11 ECLM Page (5 - 10)

## Slide 25: Why do many MOSFET devices have internally connected Zener diodes on the gates?
A. To provide a voltage reference for the correct amount of reverse-bias gate voltage
B. To protect the substrate from excessive voltages
C. To keep the gate voltage within specifications and prevent the device from overheating
D. To reduce the chance of static damage to the gate
E6A12 ECLM Page (5 - 11)

## Slide 26: Why do many MOSFET devices have internally connected Zener diodes on the gates?
A. To provide a voltage reference for the correct amount of reverse-bias gate voltage
B. To protect the substrate from excessive voltages
C. To keep the gate voltage within specifications and prevent the device from overheating
D. To reduce the chance of static damage to the gate
(D) E6A12 ECLM Page (5 - 11)

## Slide 27: What is the most useful characteristic of a Zener diode?
A. A constant current drop under conditions of varying voltage
B. A constant voltage drop under conditions of varying current
C. A negative resistance region
D. An internal capacitance that varies with the applied voltage
E6B01 ECLM Page (5 - 5)

## Slide 28: What is the most useful characteristic of a Zener diode?
A. A constant current drop under conditions of varying voltage
B. A constant voltage drop under conditions of varying current
C. A negative resistance region
D. An internal capacitance that varies with the applied voltage
(B) E6B01 ECLM Page (5 - 5)

## Slide 29: What is an important characteristic of a Schottky diode as compared to an ordinary silicon diode when used as a power supply rectifier?
A. Much higher reverse voltage breakdown
B. More constant reverse avalanche voltage
C. Longer carrier retention time
D. Less forward voltage drop
E6B02 ECLM Page (5 - 4)

## Slide 30: What is an important characteristic of a Schottky diode as compared to an ordinary silicon diode when used as a power supply rectifier?
A. Much higher reverse voltage breakdown
B. More constant reverse avalanche voltage
C. Longer carrier retention time
D. Less forward voltage drop
(D) E6B02 ECLM Page (5 - 4)

## Slide 31: What type of bias is required for an LED to emit light?
A. Reverse bias
B. Forward bias
C. Zero bias
D. Inductive bias
E6B03 ECLM Page (5 - 7)

## Slide 32: What type of bias is required for an LED to emit light?
A. Reverse bias
B. Forward bias
C. Zero bias
D. Inductive bias
(B) E6B03 ECLM Page (5 - 7)

## Slide 33: What type of semiconductor device is designed for use as a voltage-controlled capacitor?
A. Varactor diode
B. Tunnel diode
C. Silicon-controlled rectifier
D. Zener diode
E6B04 ECLM Page (5 - 6)

## Slide 34: What type of semiconductor device is designed for use as a voltage-controlled capacitor?
A. Varactor diode
B. Tunnel diode
C. Silicon-controlled rectifier
D. Zener diode
(A) E6B04 ECLM Page (5 - 6)

## Slide 35: What characteristic of a PIN diode makes it useful as an RF switch?
A. Extremely high reverse breakdown voltage
B. Ability to dissipate large amounts of power
C. Reverse bias controls its forward voltage drop
D. Low junction capacitance
E6B05 ECLM Page (5 - 7)

## Slide 36: What characteristic of a PIN diode makes it useful as an RF switch?
A. Extremely high reverse breakdown voltage
B. Ability to dissipate large amounts of power
C. Reverse bias controls its forward voltage drop
D. Low junction capacitance
(D) E6B05 ECLM Page (5 - 7)

## Slide 37: Removed from question pool Which of the following is a common use of a Schottky diode?
A. As a rectifier in high current power supplies
B. As a variable capacitance in an automatic frequency control circuit
C. As a constant voltage reference in a power supply
D. As a VHF / UHF mixer or detector
E6B06 ECLM Page (5 - 5)

## Slide 38: Removed from question pool Which of the following is a common use of a Schottky diode?
A. As a rectifier in high current power supplies
B. As a variable capacitance in an automatic frequency control circuit
C. As a constant voltage reference in a power supply
D. As a VHF / UHF mixer or detector
(D) E6B06 ECLM Page (5 - 5)

## Slide 39: What is the failure mechanism when a junction diode fails due to excessive current?
A. Excessive inverse voltage
B. Excessive junction temperature
C. Insufficient forward voltage
D. Charge carrier depletion
E6B07 ECLM Page (5 - 4)

## Slide 40: What is the failure mechanism when a junction diode fails due to excessive current?
A. Excessive inverse voltage
B. Excessive junction temperature
C. Insufficient forward voltage
D. Charge carrier depletion
(B) E6B07 ECLM Page (5 - 4)

## Slide 41: Which of the following is a Schottky barrier diode?
A. Metal-semiconductor junction
B. Electrolytic rectifier
C. PIN junction
D. Thermionic emission diode
E6B08 ECLM Page (5 - 4)

## Slide 42: Which of the following is a Schottky barrier diode?
A. Metal-semiconductor junction
B. Electrolytic rectifier
C. PIN junction
D. Thermionic emission diode
(A) E6B08 ECLM Page (5 - 4)

## Slide 43: What is a common use for point-contact diodes?
A. As a constant current source
B. As a constant voltage source
C. As an RF detector
D. As a high voltage rectifier
E6B09 ECLM Page (5 - 5)

## Slide 44: What is a common use for point-contact diodes?
A. As a constant current source
B. As a constant voltage source
C. As an RF detector
D. As a high voltage rectifier
(C) E6B09 ECLM Page (5 - 5)

## Slide 45: In Figure E6-2, what is the schematic symbol for a light-emitting diode?
A. 1
B. 5
C. 6
D. 7
E6B10 ECLM Page (5 - 7)

## Slide 46: In Figure E6-2, what is the schematic symbol for a light-emitting diode?
A. 1
B. 5
C. 6
D. 7
(B) E6B10 ECLM Page (5 - 7)

## Slide 47: What is used to control the attenuation of RF signals by a PIN diode?
A. Forward DC bias current
B. A sub-harmonic pump signal
C. Reverse voltage larger than the RF signal
D. Capacitance of an RF coupling capacitor
E6B11 ECLM Page (5 - 7)

## Slide 48: What is used to control the attenuation of RF signals by a PIN diode?
A. Forward DC bias current
B. A sub-harmonic pump signal
C. Reverse voltage larger than the RF signal
D. Capacitance of an RF coupling capacitor
(A) E6B11 ECLM Page (5 - 7)

## Slide 49: What is the function of hysteresis in a comparator?
A. To prevent input noise from causing unstable output signals
B. To allow the comparator to be used with AC input signals
C. To cause the output to change states continually
D. To increase the sensitivity
E6C01 ECLM Page (6 - 10)

## Slide 50: What is the function of hysteresis in a comparator?
A. To prevent input noise from causing unstable output signals
B. To allow the comparator to be used with AC input signals
C. To cause the output to change states continually
D. To increase the sensitivity
(A) E6C01 ECLM Page (6 - 10)

## Slide 51: What happens when the level of a comparator’s input signal crosses the threshold?
A. The IC input can be damaged
B. The comparator changes its output state
C. The comparator enters latch-up
D. The feedback loop becomes unstable
E6C02 ECLM Page (6 - 10)

## Slide 52: What happens when the level of a comparator’s input signal crosses the threshold?
A. The IC input can be damaged
B. The comparator changes its output state
C. The comparator enters latch-up
D. The feedback loop becomes unstable
(B) E6C02 ECLM Page (6 - 10)

## Slide 53: What is tri-state logic?
A. Logic devices with 0, 1, and high impedance output states
B. Logic devices that utilize ternary math
C. Low power logic devices designed to operate at 3 volts
D. Proprietary logic devices manufactured by Tri-State Devices
E6C03 ECLM Page (5 - 21)

## Slide 54: What is tri-state logic?
A. Logic devices with 0, 1, and high impedance output states
B. Logic devices that utilize ternary math
C. Low power logic devices designed to operate at 3 volts
D. Proprietary logic devices manufactured by Tri-State Devices
(A) E6C03 ECLM Page (5 - 21)

## Slide 55: Which of the following is an advantage of BiCMOS logic?
A. Its simplicity results in much less expensive devices than standard CMOS
B. It is immune to electrostatic damage
C. It has the high input impedance of CMOS and the low output impedance of bipolar transistors
D. All these choices are correct
E6C04 ECLM Page (5 - 26)

## Slide 56: Which of the following is an advantage of BiCMOS logic?
A. Its simplicity results in much less expensive devices than standard CMOS
B. It is immune to electrostatic damage
C. It has the high input impedance of CMOS and the low output impedance of bipolar transistors
D. All these choices are correct
(C) E6C04 ECLM Page (5 - 26)

## Slide 57: What is an advantage of CMOS logic devices over TTL devices?
A. Differential output capability
B. Lower distortion
C. Immune to damage from static discharge
D. Lower power consumption
E6C05 ECLM Page (5 - 26)

## Slide 58: What is an advantage of CMOS logic devices over TTL devices?
A. Differential output capability
B. Lower distortion
C. Immune to damage from static discharge
D. Lower power consumption
(D) E6C05 ECLM Page (5 - 26)

## Slide 59: Why do CMOS digital integrated circuits have high immunity to noise on the input signal or power supply?
A. Large bypass capacitance is inherent
B. The input switching threshold is about two times the power supply voltage
C. The input switching threshold is about one-half the power supply voltage
D. Bandwidth is very limited
E6C06 ECLM Page (5 - 26)

## Slide 60: Why do CMOS digital integrated circuits have high immunity to noise on the input signal or power supply?
A. Large bypass capacitance is inherent
B. The input switching threshold is about two times the power supply voltage
C. The input switching threshold is about one-half the power supply voltage
D. Bandwidth is very limited
(C) E6C06 ECLM Page (5 - 26)

## Slide 61: What best describes a pull up or pull down resistor?
A. A resistor in a keying circuit used to reduce key clicks
B. A resistor connected to the positive or negative supply line used to establish a voltage when an input or output is an open circuit
C. A resistor that ensures that an oscillator frequency does not drift
D. A resistor connected to an op-amp output that prevents signals from exceeding the power supply voltage
E6C07 ECLM Page (5 - 25)

## Slide 62: What best describes a pull up or pull down resistor?
A. A resistor in a keying circuit used to reduce key clicks
B. A resistor connected to the positive or negative supply line used to establish a voltage when an input or output is an open circuit
C. A resistor that ensures that an oscillator frequency does not drift
D. A resistor connected to an op-amp output that prevents signals from exceeding the power supply voltage
(B) E6C07 ECLM Page (5 - 25)

## Slide 63: In Figure E6-3, what is the schematic symbol for a NAND gate?
A. 1
B. 2
C. 3
D. 4
E6C08 ECLM Page (5 - 20)

## Slide 64: In Figure E6-3, what is the schematic symbol for a NAND gate?
A. 1
B. 2
C. 3
D. 4
(B) E6C08 ECLM Page (5 - 20)

## Slide 65: What is a Programmable Logic Device (PLD)?
A. A logic circuit that can be modified during use
B. A programmable collection of logic gates and circuits in a single integrated circuit
C. Programmable equipment used for testing digital logic integrated circuits
D. A type of transistor whose gain can be changed by digital logic circuits
E6C09 ECLM Page (5 - 26)

## Slide 66: What is a Programmable Logic Device (PLD)?
A. A logic circuit that can be modified during use
B. A programmable collection of logic gates and circuits in a single integrated circuit
C. Programmable equipment used for testing digital logic integrated circuits
D. A type of transistor whose gain can be changed by digital logic circuits
(B) E6C09 ECLM Page (5 - 26)

## Slide 67: In Figure E6-3, what is the schematic symbol for a NOR gate?
A. 1
B. 2
C. 3
D. 4
E6C10 ECLM Page (5 - 20)

## Slide 68: In Figure E6-3, what is the schematic symbol for a NOR gate?
A. 1
B. 2
C. 3
D. 4
(D) E6C10 ECLM Page (5 - 20)

## Slide 69: In Figure E6-3, what is the schematic symbol for the NOT operation (inverter)?
A. 2
B. 4
C. 5
D. 6
E6C11 ECLM Page (5 - 19)

## Slide 70: In Figure E6-3, what is the schematic symbol for the NOT operation (inverter)?
A. 2
B. 4
C. 5
D. 6
(C) E6C11 ECLM Page (5 - 19)