## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Which circuit is bistable?
A. An AND gate
B. An OR gate
C. A flip-flop
D. A bipolar amplifier
E7A01 ECLM Page (5 - 22)

## Slide 4: Which circuit is bistable?
A. An AND gate
B. An OR gate
C. A flip-flop
D. A bipolar amplifier
(C) E7A01 ECLM Page (5 - 22)

## Slide 5: What is the function of a decade counter?
A. It produces one output pulse for every 10 input pulses
B. It decodes a decimal number for display on a seven-segment LED display
C. It produces 10 output pulses for every input pulse
D. It decodes a binary number for display on a seven-segment LED display
E7A02 ECLM Page (5 - 24)

## Slide 6: What is the function of a decade counter?
A. It produces one output pulse for every 10 input pulses
B. It decodes a decimal number for display on a seven-segment LED display
C. It produces 10 output pulses for every input pulse
D. It decodes a binary number for display on a seven-segment LED display
(A) E7A02 ECLM Page (5 - 24)

## Slide 7: Which of the following can divide the frequency of a pulse train by 2?
A. An XOR gate
B. A flip-flop
C. An OR gate
D. A multiplexer
E7A03 ECLM Page (5 - 23)

## Slide 8: Which of the following can divide the frequency of a pulse train by 2?
A. An XOR gate
B. A flip-flop
C. An OR gate
D. A multiplexer
(B ) E7A03 ECLM Page (5 - 23)

## Slide 9: How many flip-flops are required to divide a signal frequency by 4?
A. 1
B. 2
C. 4
D. 8
E7A04 ECLM Page (5 - 23)

## Slide 10: How many flip-flops are required to divide a signal frequency by 4?
A. 1
B. 2
C. 4
D. 8
(B) E7A04 ECLM Page (5 - 23)

## Slide 11: Which of the following is a circuit that continuously alternates between two states without an external clock?
A. Monostable multivibrator
B. J-K flip-flop
C. T flip-flop
D. Astable multivibrator
E7A05 ECLM Page (5 - 23)

## Slide 12: Which of the following is a circuit that continuously alternates between two states without an external clock?
A. Monostable multivibrator
B. J-K flip-flop
C. T flip-flop
D. Astable multivibrator
(D) E7A05 ECLM Page (5 - 23)

## Slide 13: What is a characteristic of a monostable multivibrator?
A. It switches momentarily to the opposite binary state and then returns to its original state after a set time.
B. It produces a continuous square wave oscillating between 1 and 0
C. It stores one bit of data in either a 0 or 1 state
D. It maintains a constant output voltage, regardless of variations in the input voltage
E7A06 ECLM Page (5 - 23)

## Slide 14: What is a characteristic of a monostable multivibrator?
A. It switches momentarily to the opposite binary state and then returns to its original state after a set time.
B. It produces a continuous square wave oscillating between 1 and 0
C. It stores one bit of data in either a 0 or 1 state
D. It maintains a constant output voltage, regardless of variations in the input voltage
(A) E7A06 ECLM Page (5 - 23)

## Slide 15: What logical operation does a NAND gate perform?
A. It produces logic "0" at its output only when all inputs are logic "0"
B. It produces logic "1" at its output only when all inputs are logic "1"
C. It produces logic "0" at its output if some but not all of its inputs are logic "1"
D. It produces logic "0" at its output only when all inputs are logic "1"
E7A07 ECLM Page (5 - 20)

## Slide 16: What logical operation does a NAND gate perform?
A. It produces logic "0" at its output only when all inputs are logic "0"
B. It produces logic "1" at its output only when all inputs are logic "1"
C. It produces logic "0" at its output if some but not all of its inputs are logic "1"
D. It produces logic "0" at its output only when all inputs are logic "1"
(D) E7A07 ECLM Page (5 - 20)

## Slide 17: What logical operation does an OR gate perform?
A. It produces logic "1" at its output if any or all inputs are logic "1"
B. It produces logic "0" at its output if all inputs are logic "1"
C. It only produces logic "0" at its output when all inputs are logic "1"
D. It produces logic "1" at its output if all inputs are logic "0"
E7A08 ECLM Page (5 - 20)

## Slide 18: What logical operation does an OR gate perform?
A. It produces logic "1" at its output if any or all inputs are logic "1"
B. It produces logic "0" at its output if all inputs are logic "1"
C. It only produces logic "0" at its output when all inputs are logic "1"
D. It produces logic "1" at its output if all inputs are logic "0"
(A) E7A08 ECLM Page (5 - 20)

## Slide 19: What logical operation is performed by an exclusive NOR gate?
A. It produces logic 0 at its output only if all inputs are logic 0
B. It produces logic 1 at its output only if all inputs are logic 1
C. It produces logic 0 at its output if only one input is logic 1
D. It produces logic 1 at its output if only one input is logic 1
E7A09 ECLM Page (5 - 20)

## Slide 20: What logical operation is performed by an exclusive NOR gate?
A. It produces logic 0 at its output only if all inputs are logic 0
B. It produces logic 1 at its output only if all inputs are logic 1
C. It produces logic 0 at its output if only one input is logic 1
D. It produces logic 1 at its output if only one input is logic 1
(C) E7A09 ECLM Page (5 - 20)

## Slide 21: What is a truth table?
A. A table of logic symbols that indicate the high logic states of an op-amp
B. A diagram showing logic states when the digital device output is true
C. A list of inputs and corresponding outputs for a digital device
D. A table of logic symbols that indicate the logic states of an op-amp
E7A10 ECLM Page (5 - 19)

## Slide 22: What is a truth table?
A. A table of logic symbols that indicate the high logic states of an op-amp
B. A diagram showing logic states when the digital device output is true
C. A list of inputs and corresponding outputs for a digital device
D. A table of logic symbols that indicate the logic states of an op-amp
(C) E7A10 ECLM Page (5 - 19)

## Slide 23: What type of logic defines "1" as a high voltage?
A. Reverse Logic
B. Assertive Logic
C. Negative logic
D. Positive Logic
E7A11 ECLM Page (5 - 20)

## Slide 24: What type of logic defines "1" as a high voltage?
A. Reverse Logic
B. Assertive Logic
C. Negative logic
D. Positive Logic
(D) E7A11 ECLM Page (5 - 20)

## Slide 25: For what portion of the signal cycle does each active element in a push-pull Class AB amplifier conduct?
A. More than 180 degrees but less than 360 degrees
B. Exactly 180 degrees
C. The entire cycle
D. Less than 180 degrees
E7B01 ECLM Page (6 - 11)

## Slide 26: For what portion of the signal cycle does each active element in a push-pull Class AB amplifier conduct?
A. More than 180 degrees but less than 360 degrees
B. Exactly 180 degrees
C. The entire cycle
D. Less than 180 degrees
(A) E7B01 ECLM Page (6 - 11)

## Slide 27: What is a Class D amplifier?
A. A type of amplifier that uses switching technology to achieve high efficiency
B. A low power amplifier that uses a differential amplifier for improved linearity
C. An amplifier that uses drift-mode FETs for high efficiency
D. A frequency doubling amplifier
E7B02 ECLM Page (6 - 12)

## Slide 28: What is a Class D amplifier?
A. A type of amplifier that uses switching technology to achieve high efficiency
B. A low power amplifier that uses a differential amplifier for improved linearity
C. An amplifier that uses drift-mode FETs for high efficiency
D. A frequency doubling amplifier
(A) E7B02 ECLM Page (6 - 12)

## Slide 29: Which of the following components form the output of a class D amplifier circuit?
A. A low-pass filter to remove switching signal components
B. A high-pass filter to compensate for low gain at low frequencies
C. A matched load resistor to prevent damage by switching transients
D. A temperature compensating load resistor to improve linearity
E7B03 ECLM Page (6 - 12)

## Slide 30: Which of the following components form the output of a class D amplifier circuit?
A. A low-pass filter to remove switching signal components
B. A high-pass filter to compensate for low gain at low frequencies
C. A matched load resistor to prevent damage by switching transients
D. A temperature compensating load resistor to improve linearity
(A) E7B03 ECLM Page (6 - 12)

## Slide 31: Where on the load line of a Class A common emitter amplifier would bias normally be set?
A. Approximately halfway between saturation and cutoff
B. Where the load line intersects the voltage axis
C. At a point where the bias resistor equals the load resistor
D. At a point where the load line intersects the zero bias current curve
E7B04 ECLM Page (6 - 11)

## Slide 32: Where on the load line of a Class A common emitter amplifier would bias normally be set?
A. Approximately halfway between saturation and cutoff
B. Where the load line intersects the voltage axis
C. At a point where the bias resistor equals the load resistor
D. At a point where the load line intersects the zero bias current curve
(A) E7B04 ECLM Page (6 - 11)

## Slide 33: What can be done to prevent unwanted oscillations in an RF power amplifier?
A. Tune the stage for maximum SWR
B. Tune both the input and output for maximum power
C. Install parasitic suppressors and/or neutralize the stage
D. Use a phase inverter in the output filter
E7B05 ECLM Page (6 - 13)

## Slide 34: What can be done to prevent unwanted oscillations in an RF power amplifier?
A. Tune the stage for maximum SWR
B. Tune both the input and output for maximum power
C. Install parasitic suppressors and/or neutralize the stage
D. Use a phase inverter in the output filter
(C) E7B05 ECLM Page (6 - 13)

## Slide 35: Which of the following amplifier types reduces even-order harmonics?
A. Push-push
B. Push-pull
C. Class C
D. Class AB
E7B06 ECLM Page (6 - 11)

## Slide 36: Which of the following amplifier types reduces even-order harmonics?
A. Push-push
B. Push-pull
C. Class C
D. Class AB
(B) E7B06 ECLM Page (6 - 11)

## Slide 37: Which of the following is a likely result when a Class C amplifier is used to amplify a single-sideband phone signal?
A. Reduced intermodulation products
B. Increased overall intelligibility
C. Signal inversion
D. Signal distortion and excessive bandwidth
E7B07 ECLM Page (6 - 11)

## Slide 38: Which of the following is a likely result when a Class C amplifier is used to amplify a single-sideband phone signal?
A. Reduced intermodulation products
B. Increased overall intelligibility
C. Signal inversion
D. Signal distortion and excessive bandwidth
(D) E7B07 ECLM Page (6 - 11)

## Slide 39: How can an RF power amplifier be neutralized?
A. By increasing the driving power
B. By reducing the driving power
C. By feeding a 180-degree out-of-phase portion of the output back to the input
D. By feeding an in-phase component of the output back to the input
E7B08 ECLM Page (6 - 14)

## Slide 40: How can an RF power amplifier be neutralized?
A. By increasing the driving power
B. By reducing the driving power
C. By feeding a 180-degree out-of-phase portion of the output back to the input
D. By feeding an in-phase component of the output back to the input
(C) E7B08 ECLM Page (6 - 14)

## Slide 41: Which of the following describes how the loading and tuning capacitors are to be adjusted when tuning a vacuum tube RF power amplifier that employs a Pi-network output circuit?
A. The loading capacitor is set to maximum capacitance and the tuning capacitor is adjusted for minimum allowable plate current
B. The tuning capacitor is set to maximum capacitance and the loading capacitor is adjusted for minimum plate permissible current
C. The loading capacitor is adjusted to minimum plate current while alternately adjusting the tuning capacitor for maximum allowable plate current
D. The tuning capacitor is adjusted for minimum plate current, and the loading capacitor is adjusted for maximum permissible plate current
E7B09 ECLM Page (6 - 40)

## Slide 42: Which of the following describes how the loading and tuning capacitors are to be adjusted when tuning a vacuum tube RF power amplifier that employs a Pi-network output circuit?
A. The loading capacitor is set to maximum capacitance and the tuning capacitor is adjusted for minimum allowable plate current
B. The tuning capacitor is set to maximum capacitance and the loading capacitor is adjusted for minimum plate permissible current
C. The loading capacitor is adjusted to minimum plate current while alternately adjusting the tuning capacitor for maximum allowable plate current
D. The tuning capacitor is adjusted for minimum plate current, and the loading capacitor is adjusted for maximum permissible plate current
(D ) E7B09 ECLM Page (6 - 40)

## Slide 43: In Figure E7-1, what is the purpose of R1 and R2?
A. Load resistors
B. Voltage divider bias
C. Self bias
D. Feedback
E7B10 ECLM Page (6 - 3)

## Slide 44: In Figure E7-1, what is the purpose of R1 and R2?
A. Load resistors
B. Voltage divider bias
C. Self bias
D. Feedback
(B) E7B10 ECLM Page (6 - 3)

## Slide 45: In Figure E7-1, what is the purpose of R3?
A. Fixed bias
B. Emitter bypass
C. Output load resistor
D. Self bias
E7B11 ECLM Page (6 - 3)

## Slide 46: In Figure E7-1, what is the purpose of R3?
A. Fixed bias
B. Emitter bypass
C. Output load resistor
D. Self bias
(D) E7B11 ECLM Page (6 - 3)

## Slide 47: What type of amplifier circuit is shown in Figure E7-1?
A. Common base
B. Common collector
C. Common emitter
D. Emitter follower
E7B12 ECLM Page (6 - 3)

## Slide 48: What type of amplifier circuit is shown in Figure E7-1?
A. Common base
B. Common collector
C. Common emitter
D. Emitter follower
(C) E7B12 ECLM Page (6 - 3)

## Slide 49: Which of the following describes an emitter follower (or common collector) amplifier?
A. A two-transistor amplifier with the emitters sharing a common bias resistor
B. A differential amplifier with both inputs fed to the emitter of the input transistor
C. An OR circuit with only one emitter used for output
D An amplifier with a low impedance output that follows the base input voltage
E7B13 ECLM Page (6 - 4)

## Slide 50: Which of the following describes an emitter follower (or common collector) amplifier?
A. A two-transistor amplifier with the emitters sharing a common bias resistor
B. A differential amplifier with both inputs fed to the emitter of the input transistor
C. An OR circuit with only one emitter used for output
D An amplifier with a low impedance output that follows the base input voltage
(D) E7B13 ECLM Page (6 - 4)

## Slide 51: Why are switching amplifiers more efficient than linear amplifiers?
A. Switching amplifiers operate at higher voltages
B. The power transistor is at saturation or cutoff most of the time
C. Linear amplifiers have high gain resulting in higher harmonic content
D. Switching amplifiers use push-pull circuits
E7B14 ECLM Page (6 - 12)

## Slide 52: Why are switching amplifiers more efficient than linear amplifiers?
A. Switching amplifiers operate at higher voltages
B. The power transistor is at saturation or cutoff most of the time
C. Linear amplifiers have high gain resulting in higher harmonic content
D. Switching amplifiers use push-pull circuits
(B) E7B14 ECLM Page (6 - 12)

## Slide 53: What is one way to prevent thermal runaway in a bipolar transistor amplifier?
A. Neutralization
B. Select transistors with high beta
C. Use a resistor in series with the emitter
D. All of these choices are correct
E7B15 ECLM Page (6 - 3)

## Slide 54: What is one way to prevent thermal runaway in a bipolar transistor amplifier?
A. Neutralization
B. Select transistors with high beta
C. Use a resistor in series with the emitter
D. All of these choices are correct
(C) E7B15 ECLM Page (6 - 3)

## Slide 55: What is the effect of intermodulation products in a linear power amplifier?
A. Transmission of spurious signals
B. Creation of parasitic oscillations
C. Low efficiency
D. All these choices are correct
E7B16 ECLM Page (6 - 12)

## Slide 56: What is the effect of intermodulation products in a linear power amplifier?
A. Transmission of spurious signals
B. Creation of parasitic oscillations
C. Low efficiency
D. All these choices are correct
(A) E7B16 ECLM Page (6 - 12)

## Slide 57: Why are odd-order rather than even-order intermodulation distortion products of concern in linear power amplifiers?
A. Because they are relatively close in frequency to the desired signal
B. Because they are relatively far in frequency from the desired signal
C. Because they invert the sidebands causing distortion
D. Because they maintain the sidebands, thus causing multiple duplicate signals
E7B17 ECLM Page (6 - 12)

## Slide 58: Why are odd-order rather than even-order intermodulation distortion products of concern in linear power amplifiers?
A. Because they are relatively close in frequency to the desired signal
B. Because they are relatively far in frequency from the desired signal
C. Because they invert the sidebands causing distortion
D. Because they maintain the sidebands, thus causing multiple duplicate signals
(A ) E7B17 ECLM Page (6 - 12)

## Slide 59: What is a characteristic of a grounded-grid amplifier?
A. High power gain
B. High filament voltage
C. Low input impedance
D. Low bandwidth
E7B18 ECLM Page (6 - 4)

## Slide 60: What is a characteristic of a grounded-grid amplifier?
A. High power gain
B. High filament voltage
C. Low input impedance
D. Low bandwidth
(C) E7B18 ECLM Page (6 - 4)

## Slide 61: How are the capacitors and inductors of a low-pass filter Pi-network arranged between the network's input and output?
A. Two inductors are in series between the input and output, and a capacitor is connected between the two inductors and ground
B. Two capacitors are in series between the input and output, and an inductor is connected between the two capacitors and ground
C. An inductor is connected between the input and ground, another inductor is connected between the output and ground, and a capacitor is connected between the input and output
D. A capacitor is connected between the input and ground, another capacitor is connected between the output and ground, and an inductor is connected between input and output
E7C01 ECLM Page (6 - 39)

## Slide 62: How are the capacitors and inductors of a low-pass filter Pi-network arranged between the network's input and output?
A. Two inductors are in series between the input and output, and a capacitor is connected between the two inductors and ground
B. Two capacitors are in series between the input and output, and an inductor is connected between the two capacitors and ground
C. An inductor is connected between the input and ground, another inductor is connected between the output and ground, and a capacitor is connected between the input and output
D. A capacitor is connected between the input and ground, another capacitor is connected between the output and ground, and an inductor is connected between input and output
(D) E7C01 ECLM Page (6 - 39)

## Slide 63: Which of the following is a property of a T-network with series capacitors and a parallel shunt inductor?
A. It is a low-pass filter
B. It is a band-pass filter
C. It is a high-pass filter
D. It is a notch filter
E7C02 ECLM Page (6 - 40)

## Slide 64: Which of the following is a property of a T-network with series capacitors and a parallel shunt inductor?
A. It is a low-pass filter
B. It is a band-pass filter
C. It is a high-pass filter
D. It is a notch filter
(C) E7C02 ECLM Page (6 - 40)

## Slide 65: What advantage does a series-L Pi-L-network have over a series-L Pi-network for impedance matching between the final amplifier of a vacuum-tube transmitter and an antenna?
A. Greater harmonic suppression
B. Higher efficiency
C. Does not require a capacitor
D. Greater transformation range
E7C03 ECLM Page (6 - 40)

## Slide 66: What advantage does a series-L Pi-L-network have over a series-L Pi-network for impedance matching between the final amplifier of a vacuum-tube transmitter and an antenna?
A. Greater harmonic suppression
B. Higher efficiency
C. Does not require a capacitor
D. Greater transformation range
(A) E7C03 ECLM Page (6 - 40)

## Slide 67: How does an impedance-matching circuit transform a complex impedance to a resistive impedance?
A. It introduces negative resistance to cancel the resistive part of impedance
B. It introduces transconductance to cancel the reactive part of impedance
C. It cancels the reactive part of the impedance and changes the resistive part to a desired value
D. Reactive currents are dissipated in matched resistances
E7C04 ECLM Page (6 - 39)

## Slide 68: How does an impedance-matching circuit transform a complex impedance to a resistive impedance?
A. It introduces negative resistance to cancel the resistive part of impedance
B. It introduces transconductance to cancel the reactive part of impedance
C. It cancels the reactive part of the impedance and changes the resistive part to a desired value
D. Reactive currents are dissipated in matched resistances
(C) E7C04 ECLM Page (6 - 39)

## Slide 69: Which filter type is described as having ripple in the passband and a sharp cutoff?
A. A Butterworth filter
B. An active LC filter
C. A passive op-amp filter
D. A Chebyshev filter
E7C05 ECLM Page (6 - 34)

## Slide 70: Which filter type is described as having ripple in the passband and a sharp cutoff?
A. A Butterworth filter
B. An active LC filter
C. A passive op-amp filter
D. A Chebyshev filter
(D) E7C05 ECLM Page (6 - 34)

## Slide 71: What are the distinguishing features of an elliptical filter?
A. Gradual passband rolloff with minimal stop band ripple
B. Extremely flat response over its pass band with gradually rounded stop band corners
C. Extremely sharp cutoff with one or more notches in the stop band
D. Gradual passband rolloff with extreme stop band ripple
E7C06 ECLM Page (6 - 34)

## Slide 72: What are the distinguishing features of an elliptical filter?
A. Gradual passband rolloff with minimal stop band ripple
B. Extremely flat response over its pass band with gradually rounded stop band corners
C. Extremely sharp cutoff with one or more notches in the stop band
D. Gradual passband rolloff with extreme stop band ripple
(C) E7C06 ECLM Page (6 - 34)

## Slide 73: Which describes a Pi-L network used for matching a vacuum tube final amplifier to a 50-ohm unbalanced output?
A. A Phase Inverter Load network
B. A Pi-network with an additional series inductor on the output
C. A network with only three discrete parts
D. A matching network in which all components are isolated from ground
E7C07 ECLM Page (6 - 40)

## Slide 74: Which describes a Pi-L network used for matching a vacuum tube final amplifier to a 50-ohm unbalanced output?
A. A Phase Inverter Load network
B. A Pi-network with an additional series inductor on the output
C. A network with only three discrete parts
D. A matching network in which all components are isolated from ground
(B) E7C07 ECLM Page (6 - 40)

## Slide 75: Which of the following factors has the greatest effect on the bandwidth and response shape of a crystal ladder filter?
A. The relative frequencies of the individual crystals
B. The DC voltage applied to the quartz crystal
C. The gain of the RF stage preceding the filter
D. The amplitude of the signals passing through the filter
E7C08 ECLM Page (6 - 35)

## Slide 76: Which of the following factors has the greatest effect on the bandwidth and response shape of a crystal ladder filter?
A. The relative frequencies of the individual crystals
B. The DC voltage applied to the quartz crystal
C. The gain of the RF stage preceding the filter
D. The amplitude of the signals passing through the filter
(A) E7C08 ECLM Page (6 - 35)

## Slide 77: What is a crystal lattice filter?
A. A power supply filter made with interlaced quartz crystals
B. An audio filter made with four quartz crystals that resonate at 1 kHz intervals
C. A filter using lattice shaped quartz crystals for high-Q performance
D. A filter with narrow bandwidth and steep skirts made using quartz crystals
E7C09 ECLM Page (6 - 35)

## Slide 78: What is a crystal lattice filter?
A. A power supply filter made with interlaced quartz crystals
B. An audio filter made with four quartz crystals that resonate at 1 kHz intervals
C. A filter using lattice shaped quartz crystals for high-Q performance
D. A filter with narrow bandwidth and steep skirts made using quartz crystals
(D) E7C09 ECLM Page (6 - 35)

## Slide 79: Which of the following filters would be the best choice for use in a 2 meter band repeater duplexer?
A. A crystal filter
B. A cavity filter
C. A DSP filter
D. An L-C filter
E7C10 ECLM Page (6 - 33)

## Slide 80: Which of the following filters would be the best choice for use in a 2 meter band repeater duplexer?
A. A crystal filter
B. A cavity filter
C. A DSP filter
D. An L-C filter
(B) E7C10 ECLM Page (6 - 33)

## Slide 81: Which of the following describes a receiving filter's ability to reject signals occupying an adjacent channel?
A. Passband ripple
B. Phase response
C. Shape factor
D. Noise factor
E7C11 ECLM Page ( - 34)

## Slide 82: Which of the following describes a receiving filter's ability to reject signals occupying an adjacent channel?
A. Passband ripple
B. Phase response
C. Shape factor
D. Noise factor
(C) E7C11 ECLM Page ( - 34)

## Slide 83: What is one advantage of a Pi matching network over an L matching network consisting of a single inductor and a single capacitor?
A. The Q of Pi-networks can be controlled
B. L-networks cannot perform impedance transformation
C. Pi-networks are more stable
D. Pi-networks provide balanced input and output
E7C12 ECLM Page (6 - 40)

## Slide 84: What is one advantage of a Pi matching network over an L matching network consisting of a single inductor and a single capacitor?
A. The Q of Pi-networks can be controlled
B. L-networks cannot perform impedance transformation
C. Pi-networks are more stable
D. Pi-networks provide balanced input and output
(A) E7C12 ECLM Page (6 - 40)