## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Why are received spread spectrum signals resistant to interference?
A. Signals not using the spread spectrum algorithm are suppressed in the receiver
B. The high power used by a spread spectrum transmitter keeps its signal from being easily overpowered
C. The receiver is always equipped with a digital blanker
D. If interference is detected by the receiver it will signal the transmitter to change frequencies
E8D01 ECLM Page (8 - 15)

## Slide 4: Why are received spread spectrum signals resistant to interference?
A. Signals not using the spread spectrum algorithm are suppressed in the receiver
B. The high power used by a spread spectrum transmitter keeps its signal from being easily overpowered
C. The receiver is always equipped with a digital blanker
D. If interference is detected by the receiver it will signal the transmitter to change frequencies
(A) E8D01 ECLM Page (8 - 15)

## Slide 5: What spread spectrum communications technique uses a high speed binary bit stream to shift the phase of an RF carrier?
A. Frequency hopping
B. Direct sequence
C. Binary phase-shift keying
D. Phase compandored spread-spectrum
E8D02 ECLM Page (8 - 16)

## Slide 6: What spread spectrum communications technique uses a high speed binary bit stream to shift the phase of an RF carrier?
A. Frequency hopping
B. Direct sequence
C. Binary phase-shift keying
D. Phase compandored spread-spectrum
(B) E8D02 ECLM Page (8 - 16)

## Slide 7: How does the spread spectrum technique of frequency hopping work?
A. If interference is detected by the receiver it will signal the transmitter to change frequencies
B. If interference is detected by the receiver it will signal the transmitter to wait until the frequency is clear
C. A binary bit stream is used to shift the phase of an RF carrier very rapidly in a pseudorandom sequence
D. The frequency of the transmitted signal is changed very rapidly according to a pseudorandom sequence also used by the receiving station
E8D03 ECLM Page (8 - 16)

## Slide 8: How does the spread spectrum technique of frequency hopping work?
A. If interference is detected by the receiver it will signal the transmitter to change frequencies
B. If interference is detected by the receiver it will signal the transmitter to wait until the frequency is clear
C. A binary bit stream is used to shift the phase of an RF carrier very rapidly in a pseudorandom sequence
D. The frequency of the transmitted signal is changed very rapidly according to a pseudorandom sequence also used by the receiving station
(D) E8D03 ECLM Page (8 - 16)

## Slide 9: What is the primary effect of extremely short rise or fall time on a CW signal?
A. More difficult to copy
B. The generation of RF harmonics
C. The generation of key clicks
D. Limits data speed
E8D04 ECLM Page (8 - 9)

## Slide 10: What is the primary effect of extremely short rise or fall time on a CW signal?
A. More difficult to copy
B. The generation of RF harmonics
C. The generation of key clicks
D. Limits data speed
(C) E8D04 ECLM Page (8 - 9)

## Slide 11: What is the most common method of reducing key clicks?
A. Increase keying waveform rise and fall times
B. Low-pass filters at the transmitter output
C. Reduce keying waveform rise and fall times
D. High-pass filters at the transmitter output
E8D05 ECLM Page (8 - 9)

## Slide 12: What is the most common method of reducing key clicks?
A. Increase keying waveform rise and fall times
B. Low-pass filters at the transmitter output
C. Reduce keying waveform rise and fall times
D. High-pass filters at the transmitter output
(A) E8D05 ECLM Page (8 - 9)

## Slide 13: What is the advantage of including parity bits in ASCII characters?
A. Faster transmission rate
B. The signal can overpower interfering signals
C. Foreign language characters can be sent
D. Some types of errors can be detected
E8D06 ECLM Page (8 - 8)

## Slide 14: What is the advantage of including parity bits in ASCII characters?
A. Faster transmission rate
B. The signal can overpower interfering signals
C. Foreign language characters can be sent
D. Some types of errors can be detected
(D) E8D06 ECLM Page (8 - 8)

## Slide 15: What is a common cause of overmodulation of AFSK signals?
A. Excessive numbers of retries
B. Ground loops
C. Bit errors in the modem
D. Excessive transmit audio levels
E8D07 ECLM Page (8 - 14)

## Slide 16: What is a common cause of overmodulation of AFSK signals?
A. Excessive numbers of retries
B. Ground loops
C. Bit errors in the modem
D. Excessive transmit audio levels
(D) E8D07 ECLM Page (8 - 14)

## Slide 17: What parameter evaluates distortion of an AFSK signal caused by excessive input audio levels?
A. Signal to noise ratio
B. Baud rate
C. Repeat Request Rate (RRR)
D. Intermodulation Distortion (IMD)
E8D08 ECLM Page (8 - 14)

## Slide 18: What parameter evaluates distortion of an AFSK signal caused by excessive input audio levels?
A. Signal to noise ratio
B. Baud rate
C. Repeat Request Rate (RRR)
D. Intermodulation Distortion (IMD)
(D) E8D08 ECLM Page (8 - 14)

## Slide 19: What is considered an acceptable maximum IMD level for an idling PSK signal?
A. +10 dB
B. +15 dB
C. -20 dB
D. -30 dB
E8D09 ECLM Page (8 - 14)

## Slide 20: What is considered an acceptable maximum IMD level for an idling PSK signal?
A. +10 dB
B. +15 dB
C. -20 dB
D. -30 dB
(D) E8D09 ECLM Page (8 - 14)

## Slide 21: What are some of the differences between the Baudot digital code and ASCII?
A. Baudot uses 4 data bits per character, ASCII uses 7 or 8; Baudot uses 1 character as a letters/figures shift code, ASCII has no letters/figures code
B. Baudot uses 5 data bits per character, ASCII uses 7 or 8; Baudot uses 2 characters as letters/figures shift codes, ASCII has no letters/figures shift code
C. Baudot uses 6 data bits per character, ASCII uses 7 or 8; Baudot has no letters/figures shift code, ASCII uses 2 letters/figures shift codes
D. Baudot uses 7 data bits per character, ASCII uses 8; Baudot has no letters/figures shift code, ASCII uses 2 letters/figures shift codes
E8D10 ECLM Page (8 - 7)

## Slide 22: What are some of the differences between the Baudot digital code and ASCII?
A. Baudot uses 4 data bits per character, ASCII uses 7 or 8; Baudot uses 1 character as a letters/figures shift code, ASCII has no letters/figures code
B. Baudot uses 5 data bits per character, ASCII uses 7 or 8; Baudot uses 2 characters as letters/figures shift codes, ASCII has no letters/figures shift code
C. Baudot uses 6 data bits per character, ASCII uses 7 or 8; Baudot has no letters/figures shift code, ASCII uses 2 letters/figures shift codes
D. Baudot uses 7 data bits per character, ASCII uses 8; Baudot has no letters/figures shift code, ASCII uses 2 letters/figures shift codes
(B) E8D10 ECLM Page (8 - 7)

## Slide 23: What is one advantage of using ASCII code for data communications?
A. It includes built-in error correction features
B. It contains fewer information bits per character than any other code
C. It is possible to transmit both upper and lower case text
D. It uses one character as a shift code to send numeric and special characters
E8D11 ECLM Page (8 - 7)

## Slide 24: What is one advantage of using ASCII code for data communications?
A. It includes built-in error correction features
B. It contains fewer information bits per character than any other code
C. It is possible to transmit both upper and lower case text
D. It uses one character as a shift code to send numeric and special characters
(C) E8D11 ECLM Page (8 - 7)