## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: How much does the gain of an ideal parabolic dish antenna change when the operating frequency is doubled?
A. 2 dB
B. 3 dB
C. 4 dB
D. 6 dB
E9D01 ECLM Page (9 - 19)

## Slide 4: How much does the gain of an ideal parabolic dish antenna change when the operating frequency is doubled?
A. 2 dB
B. 3 dB
C. 4 dB
D. 6 dB
(D) E9D01 ECLM Page (9 - 19)

## Slide 5: How can linearly polarized Yagi antennas be used to produce circular polarization?
A. Stack two Yagis, fed 90 degrees out of phase, to form an array with the respective elements in parallel planes
B. Stack two Yagis, fed in phase, to form an array with the respective elements in parallel planes
C. Arrange two Yagis perpendicular to each other with the driven elements at the same point on the boom fed 90 degrees out of phase
D. Arrange two Yagis collinear to each other, with the driven elements fed 180 degrees out of phase
E9D02 ECLM Page (9 - 19)

## Slide 6: How can linearly polarized Yagi antennas be used to produce circular polarization?
A. Stack two Yagis, fed 90 degrees out of phase, to form an array with the respective elements in parallel planes
B. Stack two Yagis, fed in phase, to form an array with the respective elements in parallel planes
C. Arrange two Yagis perpendicular to each other with the driven elements at the same point on the boom fed 90 degrees out of phase
D. Arrange two Yagis collinear to each other, with the driven elements fed 180 degrees out of phase
(C) E9D02 ECLM Page (9 - 19)

## Slide 7: Where should a high-Q loading coil be placed to minimize losses in a shortened vertical antenna?
A. Near the center of the vertical radiator
B. As low as possible on the vertical radiator
C. As close to the transmitter as possible
D. At a voltage node
E9D03 ECLM Page (9 - 13)

## Slide 8: Where should a high-Q loading coil be placed to minimize losses in a shortened vertical antenna?
A. Near the center of the vertical radiator
B. As low as possible on the vertical radiator
C. As close to the transmitter as possible
D. At a voltage node
(A) E9D03 ECLM Page (9 - 13)

## Slide 9: Why should an HF mobile antenna loading coil have a high ratio of reactance to resistance?
A. To swamp out harmonics
B. To lower the radiation angle
C. To minimize losses
D. To minimize the Q
E9D04 ECLM Page (9 - 13)

## Slide 10: Why should an HF mobile antenna loading coil have a high ratio of reactance to resistance?
A. To swamp out harmonics
B. To lower the radiation angle
C. To minimize losses
D. To minimize the Q
(C) E9D04 ECLM Page (9 - 13)

## Slide 11: What usually occurs if a Yagi antenna is designed solely for maximum forward gain?
A. The front-to-back ratio increases
B. The front-to-back ratio decreases
C. The frequency response is widened over the whole frequency band
D. The SWR is reduced
E9D05 ECLM Page (9 - 42)

## Slide 12: What usually occurs if a Yagi antenna is designed solely for maximum forward gain?
A. The front-to-back ratio increases
B. The front-to-back ratio decreases
C. The frequency response is widened over the whole frequency band
D. The SWR is reduced
(B) E9D05 ECLM Page (9 - 42)

## Slide 13: What happens to the SWR bandwidth when one or more loading coils are used to resonate an electrically short antenna?
A. It is increased
B. It is decreased
C. It is unchanged if the loading coil is located at the feed point
D. It is unchanged if the loading coil is located at a voltage maximum point
E9D06 ECLM Page (9 - 13)

## Slide 14: What happens to the SWR bandwidth when one or more loading coils are used to resonate an electrically short antenna?
A. It is increased
B. It is decreased
C. It is unchanged if the loading coil is located at the feed point
D. It is unchanged if the loading coil is located at a voltage maximum point
(B) E9D06 ECLM Page (9 - 13)

## Slide 15: What is an advantage of using top loading in a shortened HF vertical antenna?
A. Lower Q
B. Greater structural strength
C. Higher losses
D. Improved radiation efficiency
E9D07 ECLM Page (9 - 13)

## Slide 16: What is an advantage of using top loading in a shortened HF vertical antenna?
A. Lower Q
B. Greater structural strength
C. Higher losses
D. Improved radiation efficiency
(D) E9D07 ECLM Page (9 - 13)

## Slide 17: What happens as the Q of an antenna increases?
A. SWR bandwidth increases
B. SWR bandwidth decreases
C. Gain is reduced
D. More common-mode current is present on the feed line
E9D08 ECLM Page (9 - 8)

## Slide 18: What happens as the Q of an antenna increases?
A. SWR bandwidth increases
B. SWR bandwidth decreases
C. Gain is reduced
D. More common-mode current is present on the feed line
(B) E9D08 ECLM Page (9 - 8)

## Slide 19: What is the function of a loading coil used as part of an HF mobile antenna?
A. To increase the SWR bandwidth
B. To lower the losses
C. To lower the Q
D. To cancel capacitive reactance
E9D09 ECLM Page (9 - 12)

## Slide 20: What is the function of a loading coil used as part of an HF mobile antenna?
A. To increase the SWR bandwidth
B. To lower the losses
C. To lower the Q
D. To cancel capacitive reactance
(D) E9D09 ECLM Page (9 - 12)

## Slide 21: What happens to feed point impedance at the base of a fixed length HF mobile antenna when operated below its resonant frequency?
A. The radiation resistance decreases and the capacitive reactance decreases
B. The radiation resistance decreases and the capacitive reactance increases
C. The radiation resistance increases and the capacitive reactance decreases
D. The radiation resistance increases and the capacitive reactance increases
E9D10 ECLM Page (9 - 12)

## Slide 22: What happens to feed point impedance at the base of a fixed length HF mobile antenna when operated below its resonant frequency?
A. The radiation resistance decreases and the capacitive reactance decreases
B. The radiation resistance decreases and the capacitive reactance increases
C. The radiation resistance increases and the capacitive reactance decreases
D. The radiation resistance increases and the capacitive reactance increases
(B) E9D10 ECLM Page (9 - 12)

## Slide 23: Which of the following conductors would be best for minimizing losses in a station's RF ground system?
A. Resistive wire, such as spark plug wire
B. Wide flat copper strap
C. Stranded wire
D. Solid wire
E9D11 ECLM Page (9 - 9)

## Slide 24: Which of the following conductors would be best for minimizing losses in a station's RF ground system?
A. Resistive wire, such as spark plug wire
B. Wide flat copper strap
C. Stranded wire
D. Solid wire
(B) E9D11 ECLM Page (9 - 9)

## Slide 25: Which of the following would provide the best RF ground for your station?
A. A 50-ohm resistor connected to ground
B. An electrically short connection to a metal water pipe
C. An electrically short connection to 3 or 4 interconnected ground rods driven into the Earth
D. An electrically short connection to 3 or 4 interconnected ground rods via a series RF choke
E9D12 ECLM Page (9 - 9)

## Slide 26: Which of the following would provide the best RF ground for your station?
A. A 50-ohm resistor connected to ground
B. An electrically short connection to a metal water pipe
C. An electrically short connection to 3 or 4 interconnected ground rods driven into the Earth
D. An electrically short connection to 3 or 4 interconnected ground rods via a series RF choke
(C) E9D12 ECLM Page (9 - 9)

## Slide 27: What system matches a higher impedance transmission line to a lower impedance antenna by connecting the line to the driven element in two places spaced a fraction of a wavelength each side of element center?
A. The gamma matching system
B. The delta matching system
C. The omega matching system
D. The stub matching system
E9E01 ECLM Page (9 - 25)

## Slide 28: What system matches a higher impedance transmission line to a lower impedance antenna by connecting the line to the driven element in two places spaced a fraction of a wavelength each side of element center?
A. The gamma matching system
B. The delta matching system
C. The omega matching system
D. The stub matching system
(B) E9E01 ECLM Page (9 - 25)

## Slide 29: What is the name of an antenna matching system that matches an unbalanced feed line to an antenna by feeding the driven element both at the center of the element and at a fraction of a wavelength to one side of center?
A. The gamma match
B. The delta match
C. The epsilon match
D. The stub match
E9E02 ECLM Page (9 - 25)

## Slide 30: What is the name of an antenna matching system that matches an unbalanced feed line to an antenna by feeding the driven element both at the center of the element and at a fraction of a wavelength to one side of center?
A. The gamma match
B. The delta match
C. The epsilon match
D. The stub match
(A) E9E02 ECLM Page (9 - 25)

## Slide 31: What is the name of the matching system that uses a section of transmission line connected in parallel with the feed line at or near the feed point?
A. The gamma match
B. The delta match
C. The omega match
D. The stub match
E9E03 ECLM Page (9 - 26)

## Slide 32: What is the name of the matching system that uses a section of transmission line connected in parallel with the feed line at or near the feed point?
A. The gamma match
B. The delta match
C. The omega match
D. The stub match
(D) E9E03 ECLM Page (9 - 26)

## Slide 33: What is the purpose of the series capacitor in a gamma-type antenna matching network?
A. To provide DC isolation between the feed line and the antenna
B. To cancel the inductive reactance of the matching network
C. To provide a rejection notch that prevents the radiation of harmonics
D. To transform the antenna impedance to a higher value
E9E04 ECLM Page (9 - 26)

## Slide 34: What is the purpose of the series capacitor in a gamma-type antenna matching network?
A. To provide DC isolation between the feed line and the antenna
B. To cancel the inductive reactance of the matching network
C. To provide a rejection notch that prevents the radiation of harmonics
D. To transform the antenna impedance to a higher value
(B) E9E04 ECLM Page (9 - 26)

## Slide 35: How must an antenna’s driven element be tuned to use a hairpin matching system?
A. The driven element reactance must be capacitive
B. The driven element reactance must be inductive
C. The driven element resonance must be lower than the operating frequency
D. The driven element radiation resistance must be higher than the characteristic impedance of the transmission line
E9E05 ECLM Page (9 - 38)

## Slide 36: How must an antenna’s driven element be tuned to use a hairpin matching system?
A. The driven element reactance must be capacitive
B. The driven element reactance must be inductive
C. The driven element resonance must be lower than the operating frequency
D. The driven element radiation resistance must be higher than the characteristic impedance of the transmission line
(A) E9E05 ECLM Page (9 - 38)

## Slide 37: Which of these feed line impedances would be suitable for constructing a quarter-wave Q-section for matching a 100-ohm loop to 50-ohm feed line?
A. 50 ohms
B. 62 ohms
C. 75 ohms
D. 450 ohms
E9E06 ECLM Page (9 - 38)

## Slide 38: Which of these feed line impedances would be suitable for constructing a quarter-wave Q-section for matching a 100-ohm loop to 50-ohm feed line?
A. 50 ohms
B. 62 ohms
C. 75 ohms
D. 450 ohms
(C) E9E06 ECLM Page (9 - 38)

## Slide 39: What parameter describes the interactions at the load end of a mismatched transmission line?
A. Characteristic impedance
B. Reflection coefficient
C. Velocity factor
D. Dielectric constant
E9E07 ECLM Page (9 - 31)

## Slide 40: What parameter describes the interactions at the load end of a mismatched transmission line?
A. Characteristic impedance
B. Reflection coefficient
C. Velocity factor
D. Dielectric constant
(B) E9E07 ECLM Page (9 - 31)

## Slide 41: What is a use for a Wilkinson divider?
A. It divides the operating frequency of a transmitter signal so it can be used on a lower frequency band
B. It is used to feed high-impedance antennas from a low-impedance source
C. It is used to divide power equally between two 50-ohm loads while maintaining 50-ohm input impedance
D. It is used to feed low-impedance loads from a high-impedance source
E9E08 ECLM Page (9 - 18)

## Slide 42: What is a use for a Wilkinson divider?
A. It divides the operating frequency of a transmitter signal so it can be used on a lower frequency band
B. It is used to feed high-impedance antennas from a low-impedance source
C. It is used to divide power equally between two 50-ohm loads while maintaining 50-ohm input impedance
D. It is used to feed low-impedance loads from a high-impedance source
(C) E9E08 ECLM Page (9 - 18)

## Slide 43: Which of the following is used to shunt-feed a grounded tower at its base?
A. Double-bazooka match
B. Hairpin match
C. Gamma match
D. All these choices are correct
E9E09 ECLM Page (9 - 9)

## Slide 44: Which of the following is used to shunt-feed a grounded tower at its base?
A. Double-bazooka match
B. Hairpin match
C. Gamma match
D. All these choices are correct
(C) E9E09 ECLM Page (9 - 9)

## Slide 45: Which of these choices is an effective way to match an antenna with a 100-ohm feed point impedance to a 50-ohm coaxial cable feed line?
A. Connect a 1/4-wavelength open stub of 300-ohm twinlead in parallel with the coaxial feed line where it connects to the antenna
B. Insert a 1/2-wavelength piece of 300-ohm twinlead in series between the antenna terminals and the 50-ohm feed cable
C. Insert a 1/4-wavelength piece of 75-ohm coaxial cable transmission line in series between the antenna terminals and the 50-ohm feed cable
D. Connect a 1/2 wavelength shorted stub of 75-ohm cable in parallel with the 50-ohm cable where it attaches to the antenna
E9E10 ECLM Page (9 - 39)

## Slide 46: Which of these choices is an effective way to match an antenna with a 100-ohm feed point impedance to a 50-ohm coaxial cable feed line?
A. Connect a 1/4-wavelength open stub of 300-ohm twinlead in parallel with the coaxial feed line where it connects to the antenna
B. Insert a 1/2-wavelength piece of 300-ohm twinlead in series between the antenna terminals and the 50-ohm feed cable
C. Insert a 1/4-wavelength piece of 75-ohm coaxial cable transmission line in series between the antenna terminals and the 50-ohm feed cable
D. Connect a 1/2 wavelength shorted stub of 75-ohm cable in parallel with the 50-ohm cable where it attaches to the antenna
(C) E9E10 ECLM Page (9 - 39)

## Slide 47: What is the primary purpose of phasing lines when used with an antenna having multiple driven elements?
A. It ensures that each driven element operates in concert with the others to create the desired antenna pattern
B. It prevents reflected power from traveling back down the feed line and causing harmonic radiation from the transmitter
C. It allows single-band antennas to operate on other bands
D. It creates a low-angle radiation pattern
E9E11 ECLM Page (9 - 18)

## Slide 48: What is the primary purpose of phasing lines when used with an antenna having multiple driven elements?
A. It ensures that each driven element operates in concert with the others to create the desired antenna pattern
B. It prevents reflected power from traveling back down the feed line and causing harmonic radiation from the transmitter
C. It allows single-band antennas to operate on other bands
D. It creates a low-angle radiation pattern
(A) E9E11 ECLM Page (9 - 18)

## Slide 49: What is the velocity factor of a transmission line?
A. The ratio of the characteristic impedance of the line to the terminating impedance
B. The index of shielding for coaxial cable
C. The velocity of the wave in the transmission line multiplied by the velocity of light in a vacuum
D. The velocity of the wave in the transmission line divided by the velocity of light in a vacuum
E9F01 ECLM Page (9 - 28)

## Slide 50: What is the velocity factor of a transmission line?
A. The ratio of the characteristic impedance of the line to the terminating impedance
B. The index of shielding for coaxial cable
C. The velocity of the wave in the transmission line multiplied by the velocity of light in a vacuum
D. The velocity of the wave in the transmission line divided by the velocity of light in a vacuum
(D) E9F01 ECLM Page (9 - 28)

## Slide 51: Which of the following has the biggest effect on the velocity factor of a transmission line?
A. The termination impedance
B. The line length
C. Dielectric materials used in the line
D. The center conductor resistivity
E9F02 ECLM Page (9 - 28)

## Slide 52: Which of the following has the biggest effect on the velocity factor of a transmission line?
A. The termination impedance
B. The line length
C. Dielectric materials used in the line
D. The center conductor resistivity
(C) E9F02 ECLM Page (9 - 28)

## Slide 53: Why is the physical length of a coaxial cable transmission line shorter than its electrical length?
A. Skin effect is less pronounced in the coaxial cable
B. The characteristic impedance is higher in a parallel feed line
C. The surge impedance is higher in a parallel feed line
D. Electrical signals move more slowly in a coaxial cable than in air
E9F03 ECLM Page (9 - 29)

## Slide 54: Why is the physical length of a coaxial cable transmission line shorter than its electrical length?
A. Skin effect is less pronounced in the coaxial cable
B. The characteristic impedance is higher in a parallel feed line
C. The surge impedance is higher in a parallel feed line
D. Electrical signals move more slowly in a coaxial cable than in air
(D) E9F03 ECLM Page (9 - 29)

## Slide 55: What impedance does a 1/2-wavelength transmission line present to a generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the line
D. The same as the output impedance of the generator
E9F04 ECLM Page (9 - 36)

## Slide 56: What impedance does a 1/2-wavelength transmission line present to a generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the line
D. The same as the output impedance of the generator
(B) E9F04 ECLM Page (9 - 36)

## Slide 57: What is the approximate physical length of a solid polyethylene dielectric coaxial transmission line that is electrically 1/4 wavelength long at 14.1 MHz?
A. 10.6 meters
B. 5.3 meters
C. 4.3 meters
D. 3.5 meters
E9F05 ECLM Page (9 - 29)

## Slide 58: What is the approximate physical length of a solid polyethylene dielectric coaxial transmission line that is electrically 1/4 wavelength long at 14.1 MHz?
A. 10.6 meters
B. 5.3 meters
C. 4.3 meters
D. 3.5 meters
(D) E9F05 ECLM Page (9 - 29)

## Slide 59: What is the approximate physical length of an air-insulated, parallel conductor transmission line that is electrically 1/2 wavelength long at 14.10 MHz?
A. 7.0 meters
B. 8.5 meters
C. 10.6 meters
D. 13.3 meters
E9F06 ECLM Page (9 - 30)

## Slide 60: What is the approximate physical length of an air-insulated, parallel conductor transmission line that is electrically 1/2 wavelength long at 14.10 MHz?
A. 7.0 meters
B. 8.5 meters
C. 10.6 meters
D. 13.3 meters
(C) E9F06 ECLM Page (9 - 30)

## Slide 61: How does ladder line compare to small-diameter coaxial cable such as RG-58 at 50 MHz?
A. Lower loss
B. Higher SWR
C. Smaller reflection coefficient
D. Lower velocity factor
E9F07 ECLM Page (9 - 30)

## Slide 62: How does ladder line compare to small-diameter coaxial cable such as RG-58 at 50 MHz?
A. Lower loss
B. Higher SWR
C. Smaller reflection coefficient
D. Lower velocity factor
(A) E9F07 ECLM Page (9 - 30)

## Slide 63: Which of the following is a significant difference between foam dielectric coaxial cable and solid dielectric cable, assuming all other parameters are the same?
A. Foam dielectric has lower safe operating voltage limits
B. Foam dielectric has lower loss per unit of length
C. Foam dielectric has higher velocity factor
D. All these choices are correct
E9F08 ECLM Page (9 - 31)

## Slide 64: Which of the following is a significant difference between foam dielectric coaxial cable and solid dielectric cable, assuming all other parameters are the same?
A. Foam dielectric has lower safe operating voltage limits
B. Foam dielectric has lower loss per unit of length
C. Foam dielectric has higher velocity factor
D. All these choices are correct
(D) E9F08 ECLM Page (9 - 31)

## Slide 65: What is the approximate physical length of a foam polyethylene dielectric coaxial transmission line that is electrically 1/4 wavelength long at 7.2 MHz?
A. 10.4 meters
B. 8.3 meters
C. 6.9 meters
D. 5.2 meters
E9F09 ECLM Page (9 - 29)

## Slide 66: What is the approximate physical length of a foam polyethylene dielectric coaxial transmission line that is electrically 1/4 wavelength long at 7.2 MHz?
A. 10.4 meters
B. 8.3 meters
C. 6.9 meters
D. 5.2 meters
(B) E9F09 ECLM Page (9 - 29)

## Slide 67: What impedance does a 1/8-wavelength transmission line present to a generator when the line is shorted at the far end?
A. A capacitive reactance
B. The same as the characteristic impedance of the line
C. An inductive reactance
D. Zero
E9F10 ECLM Page (9 - 37)

## Slide 68: What impedance does a 1/8-wavelength transmission line present to a generator when the line is shorted at the far end?
A. A capacitive reactance
B. The same as the characteristic impedance of the line
C. An inductive reactance
D. Zero
(C) E9F10 ECLM Page (9 - 37)

## Slide 69: What impedance does a 1/8-wavelength transmission line present to a generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. An inductive reactance
C. A capacitive reactance
D. Infinite
E9F11 ECLM Page (9 - 36)

## Slide 70: What impedance does a 1/8-wavelength transmission line present to a generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. An inductive reactance
C. A capacitive reactance
D. Infinite
(C) E9F11 ECLM Page (9 - 36)

## Slide 71: What impedance does a 1/4-wavelength transmission line present to a generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. The same as the input impedance to the generator
C. Very high impedance
D. Very low impedance
E9F12 ECLM Page (9 - 36)

## Slide 72: What impedance does a 1/4-wavelength transmission line present to a generator when the line is open at the far end?
A. The same as the characteristic impedance of the line
B. The same as the input impedance to the generator
C. Very high impedance
D. Very low impedance
(D) E9F12 ECLM Page (9 - 36)

## Slide 73: What impedance does a 1/4-wavelength transmission line present to a generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the transmission line
D. The same as the generator output impedance
E9F13 ECLM Page (9 - 36)

## Slide 74: What impedance does a 1/4-wavelength transmission line present to a generator when the line is shorted at the far end?
A. Very high impedance
B. Very low impedance
C. The same as the characteristic impedance of the transmission line
D. The same as the generator output impedance
(A) E9F13 ECLM Page (9 - 36)