## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is the primary function of an external earth connection or ground rod?
A. Reduce received noise
B. Lightning protection
C. Reduce RF current flow between pieces of equipment
D. Reduce RFI to telephones and home entertainment systems
E0A01 ECLM Page (11 - 8)

## Slide 4: What is the primary function of an external earth connection or ground rod?
A. Reduce received noise
B. Lightning protection
C. Reduce RF current flow between pieces of equipment
D. Reduce RFI to telephones and home entertainment systems
(B) E0A01 ECLM Page (11 - 8)

## Slide 5: When evaluating RF exposure levels from your station at a neighbor’s home, what must you do?
A. Ensure signals from your station are less than the controlled Maximum Permitted Exposure (MPE) limits
B. Ensure signals from your station are less than the uncontrolled Maximum Permitted Exposure (MPE) limits
C. Ensure signals from your station are less than the controlled Maximum Permitted Emission (MPE) limits
D. Ensure signals from your station are less than the uncontrolled Maximum Permitted Emission (MPE) limits
E0A02 ECLM Page (11 - 5)

## Slide 6: When evaluating RF exposure levels from your station at a neighbor’s home, what must you do?
A. Ensure signals from your station are less than the controlled Maximum Permitted Exposure (MPE) limits
B. Ensure signals from your station are less than the uncontrolled Maximum Permitted Exposure (MPE) limits
C. Ensure signals from your station are less than the controlled Maximum Permitted Emission (MPE) limits
D. Ensure signals from your station are less than the uncontrolled Maximum Permitted Emission (MPE) limits
(B) E0A02 ECLM Page (11 - 5)

## Slide 7: Over what range of frequencies are the FCC human body RF exposure limits most restrictive?
A. 300 kHz to 3 MHz
B. 3 to 30 MHz
C. 30 to 300 MHz
C. 300 to 3000 MHz
E0A03 ECLM Page (11 - 4)

## Slide 8: Over what range of frequencies are the FCC human body RF exposure limits most restrictive?
A. 300 kHz to 3 MHz
B. 3 to 30 MHz
C. 30 to 300 MHz
C. 300 to 3000 MHz
(C) E0A03 ECLM Page (11 - 4)

## Slide 9: When evaluating a site with multiple transmitters operating at the same time, the operators and licensees of which transmitters are responsible for mitigating over-exposure situations?
A. Only the most powerful transmitter
B. Only commercial transmitters
C. Each transmitter that produces 5 percent or more of its MPE limit in areas where the total MPE limit is exceeded
D. Each transmitter operating with a duty cycle greater than 50 percent
E0A04 ECLM Page (11 - 7)

## Slide 10: When evaluating a site with multiple transmitters operating at the same time, the operators and licensees of which transmitters are responsible for mitigating over-exposure situations?
A. Only the most powerful transmitter
B. Only commercial transmitters
C. Each transmitter that produces 5 percent or more of its MPE limit in areas where the total MPE limit is exceeded
D. Each transmitter operating with a duty cycle greater than 50 percent
(C) E0A04 ECLM Page (11 - 7)

## Slide 11: What is one of the potential hazards of operating in the amateur radio microwave bands?
A. Microwaves are ionizing radiation
B. The high gain antennas commonly used can result in high exposure levels
C. Microwaves often travel long distances by ionospheric reflection
D. The extremely high frequency energy can damage the joints of antenna structures
E0A05 ECLM Page (11 - 7)

## Slide 12: What is one of the potential hazards of operating in the amateur radio microwave bands?
A. Microwaves are ionizing radiation
B. The high gain antennas commonly used can result in high exposure levels
C. Microwaves often travel long distances by ionospheric reflection
D. The extremely high frequency energy can damage the joints of antenna structures
(B) E0A05 ECLM Page (11 - 7)

## Slide 13: Why are there separate electric (E) and magnetic (H) field MPE limits?
A. The body reacts to electromagnetic radiation from both the E and H fields
B. Ground reflections and scattering make the field strength vary with location
C. E field and H field radiation intensity peaks can occur at different locations
D. All these choices are correct
E0A06 ECLM Page (11 - 3)

## Slide 14: Why are there separate electric (E) and magnetic (H) field MPE limits?
A. The body reacts to electromagnetic radiation from both the E and H fields
B. Ground reflections and scattering make the field strength vary with location
C. E field and H field radiation intensity peaks can occur at different locations
D. All these choices are correct
(D) E0A06 ECLM Page (11 - 3)

## Slide 15: How may dangerous levels of carbon monoxide from an emergency generator be detected?
A. By the odor
B. Only with a carbon monoxide detector
C. Any ordinary smoke detector can be used
D. By the yellowish appearance of the gas
E0A07 ECLM Page (11 - 2)

## Slide 16: How may dangerous levels of carbon monoxide from an emergency generator be detected?
A. By the odor
B. Only with a carbon monoxide detector
C. Any ordinary smoke detector can be used
D. By the yellowish appearance of the gas
(B) E0A07 ECLM Page (11 - 2)

## Slide 17: What does SAR measure?
A. Synthetic Aperture Ratio of the human body
B. Signal Amplification Rating
C. The rate at which RF energy is absorbed by the body
D. The rate of RF energy reflected from stationary terrain
E0A08 ECLM Page (11 - 4)

## Slide 18: What does SAR measure?
A. Synthetic Aperture Ratio of the human body
B. Signal Amplification Rating
C. The rate at which RF energy is absorbed by the body
D. The rate of RF energy reflected from stationary terrain
(C) E0A08 ECLM Page (11 - 4)

## Slide 19: Which insulating material commonly used as a thermal conductor for some types of electronic devices is extremely toxic if broken or crushed and the particles are accidentally inhaled?
A. Mica
B. Zinc oxide
C. Beryllium oxide
D. Uranium Hexafluoride
E0A09 ECLM Page (11 - 2)

## Slide 20: Which insulating material commonly used as a thermal conductor for some types of electronic devices is extremely toxic if broken or crushed and the particles are accidentally inhaled?
A. Mica
B. Zinc oxide
C. Beryllium oxide
D. Uranium Hexafluoride
(C) E0A09 ECLM Page (11 - 2)

## Slide 21: What toxic material may be present in some electronic components such as high voltage capacitors and transformers?
A. Polychlorinated biphenyls
B. Polyethylene
C. Polytetrafluoroethylene
D. Polymorphic silicon
E0A10 ECLM Page (11 - 2)

## Slide 22: What toxic material may be present in some electronic components such as high voltage capacitors and transformers?
A. Polychlorinated biphenyls
B. Polyethylene
C. Polytetrafluoroethylene
D. Polymorphic silicon
(A) E0A10 ECLM Page (11 - 2)

## Slide 23: Which of the following injuries can result from using high-power UHF or microwave transmitters?
A. Hearing loss caused by high voltage corona discharge
B. Blood clotting from the intense magnetic field
C. Localized heating of the body from RF exposure in excess of the MPE limits
D. Ingestion of ozone gas from the cooling system
E0A11 ECLM Page (11 - 3)

## Slide 24: Which of the following injuries can result from using high-power UHF or microwave transmitters?
A. Hearing loss caused by high voltage corona discharge
B. Blood clotting from the intense magnetic field
C. Localized heating of the body from RF exposure in excess of the MPE limits
D. Ingestion of ozone gas from the cooling system
(C) E0A11 ECLM Page (11 - 3)