## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is the direction of an ascending pass for an amateur satellite?
A. From west to east
B. From east to west
C. From south to north
D. From north to south
E2A01 ECLM Page (2 - 9)

## Slide 4: What is the direction of an ascending pass for an amateur satellite?
A. From west to east
B. From east to west
C. From south to north
D. From north to south
(C) E2A01 ECLM Page (2 - 9)

## Slide 5: Which of the following occurs when a satellite is using an inverting linear transponder?
A. Doppler shift is reduced because the uplink and downlink shifts are in opposite directions
B. Signal position in the band is reversed
C. Upper sideband on the uplink becomes lower sideband on the downlink, and vice versa
D. All these choices are correct
E2A02 ECLM Page (2 - 11)

## Slide 6: Which of the following occurs when a satellite is using an inverting linear transponder?
A. Doppler shift is reduced because the uplink and downlink shifts are in opposite directions
B. Signal position in the band is reversed
C. Upper sideband on the uplink becomes lower sideband on the downlink, and vice versa
D. All these choices are correct
(D) E2A02 ECLM Page (2 - 11)

## Slide 7: How is the signal inverted by an inverting linear transponder?
A. The signal is detected and remodulated on the reverse sideband
B. The signal is passed through a non-linear filter
C. The signal is reduced to I and Q components and the Q component is filtered out
D. The signal is passed through a mixer and the difference rather than the sum is transmitted
E2A03 ECLM Page (2 - 11)

## Slide 8: How is the signal inverted by an inverting linear transponder?
A. The signal is detected and remodulated on the reverse sideband
B. The signal is passed through a non-linear filter
C. The signal is reduced to I and Q components and the Q component is filtered out
D. The signal is passed through a mixer and the difference rather than the sum is transmitted
(D) E2A03 ECLM Page (2 - 11)

## Slide 9: What is meant by the term "mode" as applied to an amateur radio satellite?
A. Whether the satellite is in a low earth or geostationary orbit
B. The satellite's uplink and downlink frequency bands
C. The satellite's orientation with respect to the Earth
D. Whether the satellite is in a polar or equatorial orbit
E2A04 ECLM Page (2 - 12)

## Slide 10: What is meant by the term "mode" as applied to an amateur radio satellite?
A. Whether the satellite is in a low earth or geostationary orbit
B. The satellite's uplink and downlink frequency bands
C. The satellite's orientation with respect to the Earth
D. Whether the satellite is in a polar or equatorial orbit
(B) E2A04 ECLM Page (2 - 12)

## Slide 11: What do the letters in a satellite's mode designator specify?
A. Power limits for uplink and downlink transmissions
B. The location of the ground control station
C. The polarization of uplink and downlink signals
D. The uplink and downlink frequency ranges
E2A05 ECLM Page (2 - 12)

## Slide 12: What do the letters in a satellite's mode designator specify?
A. Power limits for uplink and downlink transmissions
B. The location of the ground control station
C. The polarization of uplink and downlink signals
D. The uplink and downlink frequency ranges
(D) E2A05 ECLM Page (2 - 12)

## Slide 13: What are Keplerian elements?
A. Parameters that define the orbit of a satellite
B. Phase reversing elements in a Yagi antenna
C. High-emission heater filaments used in magnetron tubes
D. Encrypting codes used for spread-spectrum modulation
E2A06 ECLM Page (2 - 8)

## Slide 14: What are Keplerian elements?
A. Parameters that define the orbit of a satellite
B. Phase reversing elements in a Yagi antenna
C. High-emission heater filaments used in magnetron tubes
D. Encrypting codes used for spread-spectrum modulation
(A) E2A06 ECLM Page (2 - 8)

## Slide 15: Which of the following types of signals can be relayed through a linear transponder?
A. FM and CW
B. SSB and SSTV
C. PSK and packet
D. All these choices are correct
E2A07 ECLM Page (2 - 10)

## Slide 16: Which of the following types of signals can be relayed through a linear transponder?
A. FM and CW
B. SSB and SSTV
C. PSK and packet
D. All these choices are correct
(D) E2A07 ECLM Page (2 - 10)

## Slide 17: Why should effective radiated power to a satellite that uses a linear transponder be limited?
A. To prevent creating errors in the satellite telemetry
B. To avoid reducing the downlink power to all other users
C. To prevent the satellite from emitting out-of-band signals
D. To avoid interfering with terrestrial QSOs
E2A08 ECLM Page (2 - 11)

## Slide 18: Why should effective radiated power to a satellite that uses a linear transponder be limited?
A. To prevent creating errors in the satellite telemetry
B. To avoid reducing the downlink power to all other users
C. To prevent the satellite from emitting out-of-band signals
D. To avoid interfering with terrestrial QSOs
(B) E2A08 ECLM Page (2 - 11)

## Slide 19: What do the terms "L band" and "S band" specify regarding satellite communications?
A. The 23 centimeter and 13 centimeter bands
B. The 2 meter and 70 centimeter bands
C. FM and Digital Store-and-Forward systems
D. Which sideband to use
E2A09 ECLM Page (2 - 12)

## Slide 20: What do the terms "L band" and "S band" specify regarding satellite communications?
A. The 23 centimeter and 13 centimeter bands
B. The 2 meter and 70 centimeter bands
C. FM and Digital Store-and-Forward systems
D. Which sideband to use
(A) E2A09 ECLM Page (2 - 12)

## Slide 21: What type of satellite appears to stay in one position in the sky?
A. HEO
B. Geostationary
C. Geomagnetic
D. LEO
E2A10 ECLM Page (2 - 8)

## Slide 22: What type of satellite appears to stay in one position in the sky?
A. HEO
B. Geostationary
C. Geomagnetic
D. LEO
(B) E2A10 ECLM Page (2 - 8)

## Slide 23: What type of antenna can be used to minimize the effects of spin modulation and Faraday rotation?
A. A linearly polarized antenna
B. A circularly polarized antenna
C. An isotropic antenna
D. A log-periodic dipole array
E2A11 ECLM Page (2 - 9)

## Slide 24: What type of antenna can be used to minimize the effects of spin modulation and Faraday rotation?
A. A linearly polarized antenna
B. A circularly polarized antenna
C. An isotropic antenna
D. A log-periodic dipole array
(B) E2A11 ECLM Page (2 - 9)

## Slide 25: What is the purpose of digital store-and-forward functions on an amateur radio satellite?
A. To upload operational software for the transponder
B. To delay download of telemetry between satellites
C. To store digital messages in the satellite for later download by other stations
D. To relay messages between satellites
E2A12 ECLM Page (2 - 12)

## Slide 26: What is the purpose of digital store-and-forward functions on an amateur radio satellite?
A. To upload operational software for the transponder
B. To delay download of telemetry between satellites
C. To store digital messages in the satellite for later download by other stations
D. To relay messages between satellites
(C) E2A12 ECLM Page (2 - 12)

## Slide 27: Which of the following techniques is normally used by low Earth orbiting digital satellites to relay messages around the world?
A. Digipeating
B. Store-and-forward
C. Multi-satellite relaying
D. Node hopping
E2A13 ECLM Page (2 - 12)

## Slide 28: Which of the following techniques is normally used by low Earth orbiting digital satellites to relay messages around the world?
A. Digipeating
B. Store-and-forward
C. Multi-satellite relaying
D. Node hopping
(B) E2A13 ECLM Page (2 - 12)

## Slide 29: How many times per second is a new frame transmitted in a fast-scan (NTSC) television system?
A. 30
B. 60
C. 90
D. 120
E2B01 ECLM Page (8 - 19)

## Slide 30: How many times per second is a new frame transmitted in a fast-scan (NTSC) television system?
A. 30
B. 60
C. 90
D. 120
(A) E2B01 ECLM Page (8 - 19)

## Slide 31: How many horizontal lines make up a fast-scan (NTSC) television frame?
A. 30
B. 60
C. 525
D. 1080
E2B02 ECLM Page (8 - 19)

## Slide 32: How many horizontal lines make up a fast-scan (NTSC) television frame?
A. 30
B. 60
C. 525
D. 1080
(C) E2B02 ECLM Page (8 - 19)

## Slide 33: How is an interlaced scanning pattern generated in a fast-scan (NTSC) television system?
A. By scanning two fields simultaneously
B. By scanning each field from bottom to top
C. By scanning lines from left to right in one field and right to left in the next
D. By scanning odd numbered lines in one field and even numbered llines in the next
E2B03 ECLM Page (8 - 20)

## Slide 34: How is an interlaced scanning pattern generated in a fast-scan (NTSC) television system?
A. By scanning two fields simultaneously
B. By scanning each field from bottom to top
C. By scanning lines from left to right in one field and right to left in the next
D. By scanning odd numbered lines in one field and even numbered llines in the next
(D) E2B03 ECLM Page (8 - 20)

## Slide 35: How is color information sent in analog SSTV?
A. Color lines are sent sequentially
B. Color information is sent on a 2.8 kHz subcarrier
C. Color is sent in a color burst at the end of each line
D. Color is amplitude modulated on the frequency modulated intensity signal
E2B04 ECLM Page (8 - 23)

## Slide 36: How is color information sent in analog SSTV?
A. Color lines are sent sequentially
B. Color information is sent on a 2.8 kHz subcarrier
C. Color is sent in a color burst at the end of each line
D. Color is amplitude modulated on the frequency modulated intensity signal
(A) E2B04 ECLM Page (8 - 23)

## Slide 37: Which of the following describes the use of vestigial sideband in analog fast-scan TV transmissions?
A. The vestigial sideband carries the audio information
B. The vestigial sideband contains chroma information
C. Vestigial sideband reduces bandwidth while allowing for simple video detector circuitry
D. Vestigial sideband provides high frequency emphasis to sharpen the picture
E2B05 ECLM Page (8 - 21)

## Slide 38: Which of the following describes the use of vestigial sideband in analog fast-scan TV transmissions?
A. The vestigial sideband carries the audio information
B. The vestigial sideband contains chroma information
C. Vestigial sideband reduces bandwidth while allowing for simple video detector circuitry
D. Vestigial sideband provides high frequency emphasis to sharpen the picture
(C) E2B05 ECLM Page (8 - 21)

## Slide 39: What is vestigial sideband modulation?
A. Amplitude modulation in which one complete sideband and a portion of the other are transmitted
B. A type of modulation in which one sideband is inverted
C. Narrow-band FM modulation achieved by filtering one sideband from the audio before frequency modulating the carrier
D. Spread spectrum modulation achieved by applying FM modulation following single sideband amplitude modulation
E2B06 ECLM Page (8 - 21)

## Slide 40: What is vestigial sideband modulation?
A. Amplitude modulation in which one complete sideband and a portion of the other are transmitted
B. A type of modulation in which one sideband is inverted
C. Narrow-band FM modulation achieved by filtering one sideband from the audio before frequency modulating the carrier
D. Spread spectrum modulation achieved by applying FM modulation following single sideband amplitude modulation
(A) E2B06 ECLM Page (8 - 21)

## Slide 41: What is the name of the signal component that carries color information in NTSC video?
A. Luminance
B. Chroma
C. Hue
D. Spectral intensity
E2B07 ECLM Page (8 - 20)

## Slide 42: What is the name of the signal component that carries color information in NTSC video?
A. Luminance
B. Chroma
C. Hue
D. Spectral intensity
(B) E2B07 ECLM Page (8 - 20)

## Slide 43: What technique allows commercial analog TV receivers to be used for fast-scan TV operations on the 70 cm band?
A. Transmitting on channels shared with cable TV
B. Using converted satellite TV dishes
C. Transmitting on the abandoned TV channel 2
D. Using USB and demodulating the signal with a computer sound card
E2B08 ECLM Page (8 - 19)

## Slide 44: What technique allows commercial analog TV receivers to be used for fast-scan TV operations on the 70 cm band?
A. Transmitting on channels shared with cable TV
B. Using converted satellite TV dishes
C. Transmitting on the abandoned TV channel 2
D. Using USB and demodulating the signal with a computer sound card
(A) E2B08 ECLM Page (8 - 19)

## Slide 45: What hardware, other than a receiver with SSB capability and a suitable computer, is needed to decode SSTV using Digital Radio Mondiale (DRM)?
A. A special IF converter
B. A special front end limiter
C. A special notch filter to remove synchronization pulses
D. No other hardware is needed
E2B09 ECLM Page (8 - 23)

## Slide 46: What hardware, other than a receiver with SSB capability and a suitable computer, is needed to decode SSTV using Digital Radio Mondiale (DRM)?
A. A special IF converter
B. A special front end limiter
C. A special notch filter to remove synchronization pulses
D. No other hardware is needed
(D) E2B09 ECLM Page (8 - 23)

## Slide 47: What aspect of an analog slow-scan television signal encodes the brightness of the picture?
A. Tone frequency
B. Tone amplitude
C. Sync amplitude
D. Sync frequency
E2B10 ECLM Page (8 - 23)

## Slide 48: What aspect of an analog slow-scan television signal encodes the brightness of the picture?
A. Tone frequency
B. Tone amplitude
C. Sync amplitude
D. Sync frequency
(A) E2B10 ECLM Page (8 - 23)

## Slide 49: What is the function of the Vertical Interval Signaling (VIS) code sent as part of an SSTV transmission?
A. To lock the color burst oscillator in color SSTV images
B. To identify the SSTV mode being used
C. To provide vertical synchronization
D. To identify the call sign of the station transmitting
E2B11 ECLM Page (8 - 23)

## Slide 50: What is the function of the Vertical Interval Signaling (VIS) code sent as part of an SSTV transmission?
A. To lock the color burst oscillator in color SSTV images
B. To identify the SSTV mode being used
C. To provide vertical synchronization
D. To identify the call sign of the station transmitting
(B) E2B11 ECLM Page (8 - 23)

## Slide 51: What signals SSTV receiving software to begin a new picture line?
A. Specific tone frequencies
B. Elapsed time
C. Specific tone amplitudes
D. A two-tone signal
E2B12 ECLM Page (8 - 23)

## Slide 52: What signals SSTV receiving software to begin a new picture line?
A. Specific tone frequencies
B. Elapsed time
C. Specific tone amplitudes
D. A two-tone signal
(A) E2B12 ECLM Page (8 - 23)

## Slide 53: What indicator is required to be used by U.S.-licensed operators when operating a station via remote control and remote the transmitter is located in the U.S.?
A. / followed by the USPS two-letter abbreviation for the state in which the remote station is located
B. /R# where # is the district of the remote station
C. / followed by the ARRL Section of the remote station
D. No additional indicator is required
E2C01 ECLM Page (2 - 7)

## Slide 54: What indicator is required to be used by U.S.-licensed operators when operating a station via remote control and remote the transmitter is located in the U.S.?
A. / followed by the USPS two-letter abbreviation for the state in which the remote station is located
B. /R# where # is the district of the remote station
C. / followed by the ARRL Section of the remote station
D. No additional indicator is required
(D) E2C01 ECLM Page (2 - 7)

## Slide 55: Which of the following best describes the term "self-spotting" in connection with HF contest operating?
A. The often-prohibited practice of posting one’s own call sign and frequency on a spotting network
B. The acceptable practice of manually posting the call signs of stations on a spotting network
C. A manual technique for rapidly zero beating or tuning to a station’s frequency before calling that station
D. An automatic method for rapidly zero beating or tuning to a station’s frequency before calling that station
E2C02 ECLM Page (2 - 7)

## Slide 56: Which of the following best describes the term "self-spotting" in connection with HF contest operating?
A. The often-prohibited practice of posting one’s own call sign and frequency on a spotting network
B. The acceptable practice of manually posting the call signs of stations on a spotting network
C. A manual technique for rapidly zero beating or tuning to a station’s frequency before calling that station
D. An automatic method for rapidly zero beating or tuning to a station’s frequency before calling that station
(A) E2C02 ECLM Page (2 - 7)

## Slide 57: From which of the following bands is amateur radio contesting generally excluded?
A. 30 meters
B. 6 meters
C. 2 meters
D. 33 centimeters
E2C03 ECLM Page (2 - 6)

## Slide 58: From which of the following bands is amateur radio contesting generally excluded?
A. 30 meters
B. 6 meters
C. 2 meters
D. 33 centimeters
(A ) E2C03 ECLM Page (2 - 6)

## Slide 59: Which of the following frequencies are sometimes used for amateur radio mesh networks?
A. HF frequencies where digital communications are permitted
B. Frequencies shared with various unlicensed wireless data services
C. Cable TV channels 41 through 43
D. The 60 meter band channel centered on 5373 kHz
E2C04 ECLM Page (8 - 16)

## Slide 60: Which of the following frequencies are sometimes used for amateur radio mesh networks?
A. HF frequencies where digital communications are permitted
B. Frequencies shared with various unlicensed wireless data services
C. Cable TV channels 41 through 43
D. The 60 meter band channel centered on 5373 kHz
(B) E2C04 ECLM Page (8 - 16)

## Slide 61: What is the function of a DX QSL Manager?
A. To allocate frequencies for DXpeditions
B. To handle the receiving and sending of confirmation cards for a DX station
C. To run a net to allow many stations to contact a rare DX station
D. To relay calls to and from a DX station
E2C05 ECLM Page (2 - 3)

## Slide 62: What is the function of a DX QSL Manager?
A. To allocate frequencies for DXpeditions
B. To handle the receiving and sending of confirmation cards for a DX station
C. To run a net to allow many stations to contact a rare DX station
D. To relay calls to and from a DX station
(B) E2C05 ECLM Page (2 - 3)

## Slide 63: During a VHF/UHF contest, in which band segment would you expect to find the highest level of SSB or CW activity?
A. At the top of each band, usually in a segment reserved for contests
B. In the middle of each band, usually on the national calling frequency
C. In the weak signal segment of the band, with most of the activity near the calling frequency
D. In the middle of the band, usually 25 kHz above the national calling frequency
E2C06 ECLM Page (2 - 6)

## Slide 64: During a VHF/UHF contest, in which band segment would you expect to find the highest level of SSB or CW activity?
A. At the top of each band, usually in a segment reserved for contests
B. In the middle of each band, usually on the national calling frequency
C. In the weak signal segment of the band, with most of the activity near the calling frequency
D. In the middle of the band, usually 25 kHz above the national calling frequency
(C) E2C06 ECLM Page (2 - 6)

## Slide 65: What is the Cabrillo format?
A. A standard for submission of electronic contest logs
B. A method of exchanging information during a contest QSO
C. The most common set of contest rules
D. The rules of order for meetings between contest sponsors
E2C07 ECLM Page (2 - 6)

## Slide 66: What is the Cabrillo format?
A. A standard for submission of electronic contest logs
B. A method of exchanging information during a contest QSO
C. The most common set of contest rules
D. The rules of order for meetings between contest sponsors
(A) E2C07 ECLM Page (2 - 6)

## Slide 67: Which of the following contacts may be confirmed through the U.S. QSL bureau system?
A. Special event contacts between stations in the U.S.
B. Contacts between a U.S. station and a non-U.S. station
C. Repeater contacts between U.S. club members
D. Contacts using tactical call signs
E2C08 ECLM Page (2 - 3)

## Slide 68: Which of the following contacts may be confirmed through the U.S. QSL bureau system?
A. Special event contacts between stations in the U.S.
B. Contacts between a U.S. station and a non-U.S. station
C. Repeater contacts between U.S. club members
D. Contacts using tactical call signs
(B) E2C08 ECLM Page (2 - 3)

## Slide 69: What type of equipment is commonly used to implement an amateur radio mesh network?
A. A 2 meter VHF transceiver with a 1200 baud modem
B. An optical cable connection between the USB ports of 2 separate computers
C. A wireless router running custom firmware
D. A 440 MHz transceiver with a 9600 baud modem
E2C09 ECLM Page (8 - 16)

## Slide 70: What type of equipment is commonly used to implement an amateur radio mesh network?
A. A 2 meter VHF transceiver with a 1200 baud modem
B. An optical cable connection between the USB ports of 2 separate computers
C. A wireless router running custom firmware
D. A 440 MHz transceiver with a 9600 baud modem
(C) E2C09 ECLM Page (8 - 16)

## Slide 71: Why might a DX station state that they are listening on another frequency?
A. Because the DX station may be transmitting on a frequency that is prohibited to some responding stations
B. To separate the calling stations from the DX station
C. To improve operating efficiency by reducing interference
D. All these choices are correct
E2C10 ECLM Page (2 - 4)

## Slide 72: Why might a DX station state that they are listening on another frequency?
A. Because the DX station may be transmitting on a frequency that is prohibited to some responding stations
B. To separate the calling stations from the DX station
C. To improve operating efficiency by reducing interference
D. All these choices are correct
(D) E2C10 ECLM Page (2 - 4)

## Slide 73: How should you generally identify your station when attempting to contact a DX station during a contest or in a pileup?
A. Send your full call sign once or twice
B. Send only the last two letters of your call sign until you make contact
C. Send your full call sign and grid square
D. Send the call sign of the DX station three times, the words "this is," then your call sign three times
E2C11 ECLM Page (2 - 4)

## Slide 74: How should you generally identify your station when attempting to contact a DX station during a contest or in a pileup?
A. Send your full call sign once or twice
B. Send only the last two letters of your call sign until you make contact
C. Send your full call sign and grid square
D. Send the call sign of the DX station three times, the words "this is," then your call sign three times
(A) E2C11 ECLM Page (2 - 4)

## Slide 75: What technique do individual nodes use to form a mesh network?
A. Forward error correction and Viterbi codes
B. Acting as store-and-forward digipeaters
C. Discovery and link establishment protocols
D. Custom code plugs for the local trunking systems
E2C12 ECLM Page (8 - 16)

## Slide 76: What technique do individual nodes use to form a mesh network?
A. Forward error correction and Viterbi codes
B. Acting as store-and-forward digipeaters
C. Discovery and link establishment protocols
D. Custom code plugs for the local trunking systems
(C) E2C12 ECLM Page (8 - 16)