## Slide 2
Extra License Manual
and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: What is the name of the process that shows that a square wave is made up of a sine wave plus all its odd harmonics?
A. Fourier analysis
B. Vector analysis
C. Numerical analysis
D. Differential analysis
E8A01 ECLM Page (7 - 8)

## Slide 4: What is the name of the process that shows that a square wave is made up of a sine wave plus all its odd harmonics?
A. Fourier analysis
B. Vector analysis
C. Numerical analysis
D. Differential analysis
(A) E8A01 ECLM Page (7 - 8)

## Slide 5: Which of the following is a type of analog-to-digital conversion?
A. Successive approximation
B. Harmonic regeneration
C. Level shifting
D. Phase reversal
E8A02 ECLM Page (6 - 30)

## Slide 6: Which of the following is a type of analog-to-digital conversion?
A. Successive approximation
B. Harmonic regeneration
C. Level shifting
D. Phase reversal
(A) E8A02 ECLM Page (6 - 30)

## Slide 7: What type of wave does a Fourier analysis show to be made up of sine waves of a given fundamental frequency plus all its harmonics?
A. A sawtooth wave
B. A square wave
C. A sine wave
D. A cosine wave
E8A03 ECLM Page (7 - 9)

## Slide 8: What type of wave does a Fourier analysis show to be made up of sine waves of a given fundamental frequency plus all its harmonics?
A. A sawtooth wave
B. A square wave
C. A sine wave
D. A cosine wave
(A) E8A03 ECLM Page (7 - 9)

## Slide 9: What is "dither" with respect to analog -to-digital converters?
A. An abnormal condition where the converter cannot settle on a value to represent the signal
B. A small amount of noise added to the input signal to allow more precise representation of a signal over time
C. An error caused by irregular quantization step size
D. A method of decimation by randomly skipping samples
E8A04 ECLM Page (6 - 28)

## Slide 10: What is "dither" with respect to analog -to-digital converters?
A. An abnormal condition where the converter cannot settle on a value to represent the signal
B. A small amount of noise added to the input signal to allow more precise representation of a signal over time
C. An error caused by irregular quantization step size
D. A method of decimation by randomly skipping samples
(B) E8A04 ECLM Page (6 - 28)

## Slide 11: What of the following instruments would be the most accurate for measuring the RMS voltage of a complex waveform?
A. A grid dip meter
B. A D'Arsonval meter
C. An absorption wavemeter
D. A true-RMS calculating meter
E8A05 ECLM Page (7 - 2)

## Slide 12: What of the following instruments would be the most accurate for measuring the RMS voltage of a complex waveform?
A. A grid dip meter
B. A D'Arsonval meter
C. An absorption wavemeter
D. A true-RMS calculating meter
(D) E8A05 ECLM Page (7 - 2)

## Slide 13: What is the approximate ratio of PEP-to-average power in a typical single-sideband phone signal?
A. 2.5 to 1
B. 25 to 1
C. 1 to 1
D. 100 to 1
E8A06 ECLM Page (7 - 3)

## Slide 14: What is the approximate ratio of PEP-to-average power in a typical single-sideband phone signal?
A. 2.5 to 1
B. 25 to 1
C. 1 to 1
D. 100 to 1
(A ) E8A06 ECLM Page (7 - 3)

## Slide 15: What determines the PEP-to-average power ratio of a single-sideband phone signal?
A. The frequency of the modulating signal
B. Speech characteristics
C. The degree of carrier suppression
D. Amplifier gain
E8A07 ECLM Page (7 - 3)

## Slide 16: What determines the PEP-to-average power ratio of a single-sideband phone signal?
A. The frequency of the modulating signal
B. Speech characteristics
C. The degree of carrier suppression
D. Amplifier gain
(B) E8A07 ECLM Page (7 - 3)

## Slide 17: Why would a direct or flash conversion analog-to-digital converter be useful for a software defined radio?
A. Very low power consumption decreases frequency drift
B. Immunity to out of sequence coding reduces spurious responses
C. Very high speed allows digitizing high frequencies
D. All these choices are correct
E8A08 ECLM Page (6 - 29)

## Slide 18: Why would a direct or flash conversion analog-to-digital converter be useful for a software defined radio?
A. Very low power consumption decreases frequency drift
B. Immunity to out of sequence coding reduces spurious responses
C. Very high speed allows digitizing high frequencies
D. All these choices are correct
(C) E8A08 ECLM Page (6 - 29)

## Slide 19: How many different input levels can be encoded by an analog-to-digital converter with 8-bit resolution?
A. 8
B. 8 multiplied by the gain of the input amplifier
C. 256 divided by the gain of the input amplifier
D. 256
E8A09 ECLM Page (6 - 27)

## Slide 20: How many different input levels can be encoded by an analog-to-digital converter with 8-bit resolution?
A. 8
B. 8 multiplied by the gain of the input amplifier
C. 256 divided by the gain of the input amplifier
D. 256
(D) E8A09 ECLM Page (6 - 27)

## Slide 21: What is the purpose of a low pass filter used in conjunction with a digital-to-analog converter?
A. Lower the input bandwidth to increase the effective resolution
B. Improve accuracy by removing out of sequence codes from the input
C. Remove harmonics from the output caused by the discrete analog levels generated
D. All these choices are correct
E8A10 ECLM Page (6 - 28)

## Slide 22: What is the purpose of a low pass filter used in conjunction with a digital-to-analog converter?
A. Lower the input bandwidth to increase the effective resolution
B. Improve accuracy by removing out of sequence codes from the input
C. Remove harmonics from the output caused by the discrete analog levels generated
D. All these choices are correct
(C) E8A10 ECLM Page (6 - 28)

## Slide 23: Which of the following is a measure of the quality of an analog-to-digital converter?
A. Total harmonic distortion
B. Peak envelope power
C. Reciprocal mixing
D. Power factor
E8A11 ECLM Page (6 - 28)

## Slide 24: Which of the following is a measure of the quality of an analog-to-digital converter?
A. Total harmonic distortion
B. Peak envelope power
C. Reciprocal mixing
D. Power factor
(A) E8A11 ECLM Page (6 - 28)

## Slide 25: What is the modulation index of an FM signal?
A. The ratio of frequency deviation to modulating signal frequency
B. The ratio of modulating signal amplitude to frequency deviation
C. The type of modulation used by the transmitter
D. The bandwidth of the transmitted signal divided by the modulating signal frequency
E8B01 ECLM Page (8 - 3)

## Slide 26: What is the modulation index of an FM signal?
A. The ratio of frequency deviation to modulating signal frequency
B. The ratio of modulating signal amplitude to frequency deviation
C. The type of modulation used by the transmitter
D. The bandwidth of the transmitted signal divided by the modulating signal frequency
(A) E8B01 ECLM Page (8 - 3)

## Slide 27: How does the modulation index of a phase-modulated emission vary with RF carrier frequency?
A. It increases as the RF carrier frequency increases
B. It decreases as the RF carrier frequency increases
C. It varies with the square root of the RF carrier frequency
D. It does not depend on the RF carrier frequency
E8B02 ECLM Page (8 - 4)

## Slide 28: How does the modulation index of a phase-modulated emission vary with RF carrier frequency?
A. It increases as the RF carrier frequency increases
B. It decreases as the RF carrier frequency increases
C. It varies with the square root of the RF carrier frequency
D. It does not depend on the RF carrier frequency
(D) E8B02 ECLM Page (8 - 4)

## Slide 29: What is the modulation index of an FM-phone signal having a maximum frequency deviation of 3000 Hz either side of the carrier frequency, when the modulating frequency is 1000 Hz?
A. 3
B. 0.3
C. 3000
D. 1000
E8B03 ECLM Page (8 - 4)

## Slide 30: What is the modulation index of an FM-phone signal having a maximum frequency deviation of 3000 Hz either side of the carrier frequency, when the modulating frequency is 1000 Hz?
A. 3
B. 0.3
C. 3000
D. 1000
(A) E8B03 ECLM Page (8 - 4)

## Slide 31: What is the modulation index of an FM-phone signal having a maximum carrier deviation of plus or minus 6 kHz when modulated with a 2-kHz modulating frequency?
A. 6000
B. 3
C. 2000
D. 1/3
E8B04 ECLM Page (8 - 4)

## Slide 32: What is the modulation index of an FM-phone signal having a maximum carrier deviation of plus or minus 6 kHz when modulated with a 2-kHz modulating frequency?
A. 6000
B. 3
C. 2000
D. 1/3
(B) E8B04 ECLM Page (8 - 4)

## Slide 33: What is the deviation ratio of an FM-phone signal having a maximum frequency swing of plus-or-minus 5 kHz when the maximum modulation frequency is 3 kHz?
A. 60
B. 0.167
C. 0.6
D. 1.67
E8B05 ECLM Page (8 - 3)

## Slide 34: What is the deviation ratio of an FM-phone signal having a maximum frequency swing of plus-or-minus 5 kHz when the maximum modulation frequency is 3 kHz?
A. 60
B. 0.167
C. 0.6
D. 1.67
(D) E8B05 ECLM Page (8 - 3)

## Slide 35: What is the deviation ratio of an FM-phone signal having a maximum frequency swing of plus or minus 7.5 kHz when the maximum modulation frequency is 3.5 kHz?
A. 2.14
B. 0.214
C. 0.47
D. 47
E8B06 ECLM Page (8 - 3)

## Slide 36: What is the deviation ratio of an FM-phone signal having a maximum frequency swing of plus or minus 7.5 kHz when the maximum modulation frequency is 3.5 kHz?
A. 2.14
B. 0.214
C. 0.47
D. 47
(A) E8B06 ECLM Page (8 - 3)

## Slide 37: Orthogonal Frequency Division Multiplexing is a technique used for which type of amateur communication?
A. High-speed digital modes
B. Extremely low-power contacts
C. EME
D. OFDM signals are not allowed on amateur bands
E8B07 ECLM Page (8 - 14)

## Slide 38: Orthogonal Frequency Division Multiplexing is a technique used for which type of amateur communication?
A. High-speed digital modes
B. Extremely low-power contacts
C. EME
D. OFDM signals are not allowed on amateur bands
(A) E8B07 ECLM Page (8 - 14)

## Slide 39: What describes Orthogonal Frequency Division Multiplexing?
A. A frequency modulation technique that uses non-harmonically related frequencies
B. A bandwidth compression technique using Fourier transforms
C. A digital mode for narrow band, slow speed transmissions
D. A digital modulation technique using subcarriers at frequencies chosen to avoid intersymbol interference
E8B08 ECLM Page (8 - 14)

## Slide 40: What describes Orthogonal Frequency Division Multiplexing?
A. A frequency modulation technique that uses non-harmonically related frequencies
B. A bandwidth compression technique using Fourier transforms
C. A digital mode for narrow band, slow speed transmissions
D. A digital modulation technique using subcarriers at frequencies chosen to avoid intersymbol interference
(D) E8B08 ECLM Page (8 - 14)

## Slide 41: What is deviation ratio?
A. The ratio of the audio modulating frequency to the center carrier frequency
B. The ratio of the maximum carrier frequency deviation to the highest audio modulating frequency
C. The ratio of the carrier center frequency to the audio modulating frequency
D. The ratio of the highest audio modulating frequency to the average audio modulating frequency
E8B09 ECLM Page (8 - 3)

## Slide 42: What is deviation ratio?
A. The ratio of the audio modulating frequency to the center carrier frequency
B. The ratio of the maximum carrier frequency deviation to the highest audio modulating frequency
C. The ratio of the carrier center frequency to the audio modulating frequency
D. The ratio of the highest audio modulating frequency to the average audio modulating frequency
(B) E8B09 ECLM Page (8 - 3)

## Slide 43: What is frequency division multiplexing?
A. The transmitted signal jumps from band to band at a predetermined rate
B. Two or more information streams are merged into a baseband, which then modulates the transmitter
C. The transmitted signal is divided into packets of information
D. Two or more information streams are merged into a digital combiner, which then pulse position modulates the transmitter
E8B10 ECLM Page (8 - 5)

## Slide 44: What is frequency division multiplexing?
A. The transmitted signal jumps from band to band at a predetermined rate
B. Two or more information streams are merged into a baseband, which then modulates the transmitter
C. The transmitted signal is divided into packets of information
D. Two or more information streams are merged into a digital combiner, which then pulse position modulates the transmitter
(B) E8B10 ECLM Page (8 - 5)

## Slide 45: What is digital time division multiplexing?
A. Two or more data streams are assigned to discrete sub-carriers on an FM transmitter
B. Two or more signals are arranged to share discrete time slots of a data transmission
C. Two or more data streams share the same channel by transmitting time of transmission as the sub-carrier
D. Two or more signals are quadrature modulated to increase bandwidth efficiency
E8B11 ECLM Page (8 - 5)

## Slide 46: What is digital time division multiplexing?
A. Two or more data streams are assigned to discrete sub-carriers on an FM transmitter
B. Two or more signals are arranged to share discrete time slots of a data transmission
C. Two or more data streams share the same channel by transmitting time of transmission as the sub-carrier
D. Two or more signals are quadrature modulated to increase bandwidth efficiency
(B) E8B11 ECLM Page (8 - 5)

## Slide 47: How is Forward Error Correction implemented?
A. By the receiving station repeating each block of three data characters
B. By transmitting a special algorithm to the receiving station along with the data characters
C. By transmitting extra data that may be used to detect and correct transmission errors
D. By varying the frequency shift of the transmitted signal according to a predefined algorithm
E8C01 ECLM Page (8 - 17)

## Slide 48: How is Forward Error Correction implemented?
A. By the receiving station repeating each block of three data characters
B. By transmitting a special algorithm to the receiving station along with the data characters
C. By transmitting extra data that may be used to detect and correct transmission errors
D. By varying the frequency shift of the transmitted signal according to a predefined algorithm
(C) E8C01 ECLM Page (8 - 17)

## Slide 49: What is the definition of symbol rate in a digital transmission?
A. The number of control characters in a message packet
B. The duration of each bit in a message sent over the air
C. The rate at which the waveform changes to convey information
D. The number of characters carried per second by the station-to-station link
E8C02 ECLM Page (8 - 5)

## Slide 50: What is the definition of symbol rate in a digital transmission?
A. The number of control characters in a message packet
B. The duration of each bit in a message sent over the air
C. The rate at which the waveform changes to convey information
D. The number of characters carried per second by the station-to-station link
(C) E8C02 ECLM Page (8 - 5)

## Slide 51: Why should phase-shifting of a PSK signal be done at the zero crossing of the RF signal?
A. To minimize bandwidth
B. To simplify modulation
C. To improve carrier suppression
D. All these choices are correct
E8C03 ECLM Page (8 - 11)

## Slide 52: Why should phase-shifting of a PSK signal be done at the zero crossing of the RF signal?
A. To minimize bandwidth
B. To simplify modulation
C. To improve carrier suppression
D. All these choices are correct
(A ) E8C03 ECLM Page (8 - 11)

## Slide 53: What technique minimizes the bandwidth of a PSK31 signal?
A. Zero-sum character encoding
B. Reed-Solomon character encoding
C. Use of sinusoidal data pulses
D. Use of trapezoidal data pulses
E8C04 ECLM Page (8 - 11)

## Slide 54: What technique minimizes the bandwidth of a PSK31 signal?
A. Zero-sum character encoding
B. Reed-Solomon character encoding
C. Use of sinusoidal data pulses
D. Use of trapezoidal data pulses
(C) E8C04 ECLM Page (8 - 11)

## Slide 55: What is the approximate bandwidth of a 13-WPM International Morse Code transmission?
A. 13 Hz
B. 26 Hz
C. 52 Hz
D. 104 Hz
E8C05 ECLM Page (8 - 9)

## Slide 56: What is the approximate bandwidth of a 13-WPM International Morse Code transmission?
A. 13 Hz
B. 26 Hz
C. 52 Hz
D. 104 Hz
(C) E8C05 ECLM Page (8 - 9)

## Slide 57: What is the bandwidth of a 170-hertz shift, 300-baud ASCII transmission?
A. 0.1 Hz
B. 0.3 kHz
C. 0.5 kHz
D. 1.0 kHz
E8C06 ECLM Page (8 - 10)

## Slide 58: What is the bandwidth of a 170-hertz shift, 300-baud ASCII transmission?
A. 0.1 Hz
B. 0.3 kHz
C. 0.5 kHz
D. 1.0 kHz
(C) E8C06 ECLM Page (8 - 10)

## Slide 59: What is the bandwidth of a 4800-Hz frequency shift, 9600-baud ASCII FM transmission?
A. 15.36 kHz
B. 9.6 kHz
C. 4.8 kHz
D. 5.76 kHz
E8C07 ECLM Page (8 - 10)

## Slide 60: What is the bandwidth of a 4800-Hz frequency shift, 9600-baud ASCII FM transmission?
A. 15.36 kHz
B. 9.6 kHz
C. 4.8 kHz
D. 5.76 kHz
(A ) E8C07 ECLM Page (8 - 10)

## Slide 61: How does ARQ accomplish error correction?
A. Special binary codes provide automatic correction
B. Special polynomial codes provide automatic correction
C. If errors are detected, redundant data is substituted
D. If errors are detected, a retransmission is requested
E8C08 ECLM Page (8 - 17)

## Slide 62: How does ARQ accomplish error correction?
A. Special binary codes provide automatic correction
B. Special polynomial codes provide automatic correction
C. If errors are detected, redundant data is substituted
D. If errors are detected, a retransmission is requested
(D) E8C08 ECLM Page (8 - 17)

## Slide 63: Which digital code allows only one bit to change between sequential code values?
A. Binary Coded Decimal Code
B. Extended Binary Coded Decimal Interchange Code
C. Excess 3 code
D. Gray code
E8C09 ECLM Page (8 - 8)

## Slide 64: Which digital code allows only one bit to change between sequential code values?
A. Binary Coded Decimal Code
B. Extended Binary Coded Decimal Interchange Code
C. Excess 3 code
D. Gray code
(D) E8C09 ECLM Page (8 - 8)

## Slide 65: How may data rate be increased without increasing bandwidth?
A. It is impossible
B. Increasing analog-to-digital conversion resolution
C. Using a more efficient digital code
D. Using forward error correction
E8C10 ECLM Page (8 - 6)

## Slide 66: How may data rate be increased without increasing bandwidth?
A. It is impossible
B. Increasing analog-to-digital conversion resolution
C. Using a more efficient digital code
D. Using forward error correction
(C) E8C10 ECLM Page (8 - 6)

## Slide 67: What is the relationship between symbol rate and baud?
A. They are the same
B. Baud is twice the symbol rate
C. Symbol rate is only used for packet-based modes
D. Baud is only used for RTTY
E8C11 ECLM Page (8 - 5)

## Slide 68: What is the relationship between symbol rate and baud?
A. They are the same
B. Baud is twice the symbol rate
C. Symbol rate is only used for packet-based modes
D. Baud is only used for RTTY
(A) E8C11 ECLM Page (8 - 5)

## Slide 69: What factors affect the bandwidth of a transmitted CW signal?
A. IF bandwidth and Q
B. Modulation index and output power
C. Keying speed and shape factor (rise and fall time)
D. All these choices are correct
E8C12 ECLM Page (8 - 9)

## Slide 70: What factors affect the bandwidth of a transmitted CW signal?
A. IF bandwidth and Q
B. Modulation index and output power
C. Keying speed and shape factor (rise and fall time)
D. All these choices are correct
(C) E8C12 ECLM Page (8 - 9)